## Slide 1: Periodic task scheduling
An exact test for EDF
Relative deadlines less than periods
Processor demand criterion
1

## Slide 2: The earliest deadline first policy
Optimal scheduling policy when relative deadlines are equal to task periods
Is a task-dynamic priority policy (but not job-dynamic)
How does it behave when relative deadlines are less than periods?
Exact analysis for EDF
2

## Slide 3: Why not analyze task interference as we did with DM?
Interference is due to only those jobs with earlier absolute deadlines
Task j exercises interference on task i, and task i exercises interference on task j
Interference relations are complex due to dynamic priorities  will abandon this view
Pj
Cj
Pi
Di
Ri
Dj
3

## Slide 4: EDF and processor demand
Task i requests service (work) Ci at every arrival ri,k
A request becomes demand only at the deadline di,k
  Before the deadline, we are not obliged to complete the request
4

## Slide 5: EDF and processor demand
Task i requests service (work) Ci at every arrival ri,k
What is the demand in [0, L] for L > 0? (t1= 0 and t2 = L)
5
Pi
Di
L
Pi = Di
L

## Slide 6: EDF and processor demand
Consider demand on the processor due to tasks whose deadlines have passed
Within any time interval, L, the demand must be less than L.
Pj
Cj
Pi
Di
Dj
L
6
The execution time demanded
by jobs with deadline less than L over an interval of length L cannot be greater than L
Notes: Demand of task i in interval [0, L] is . Why ?
Well, we want to count the number of jobs that arrived in [0,L] and whose absolute deadlines is <= L
Demand in only contributions from jobs that finished before L (remember requests become demands (need to be complete for feasibility) at deadline boundaries)
This quantity is
Demand of task i in interval [0, L] is ⌊(𝐿+𝑃_𝑖−𝐷_𝑖)/𝑃_𝑖 ⌋. Why ?
Well, we want to count the number of jobs that arrived in [0,L] and whose absolute deadlines is <= L
Demand in only contributions from jobs that finished before L (remember requests become demands (need to be complete for feasibility) at deadline boundaries)
This quantity is
max{𝑘≥0:𝑑_(𝑖,𝑘)≤𝐿}=max{𝑘≥0:𝑟_(𝑖,𝑘)+𝐷_𝑖≤𝐿}=max{𝑘≥0: (𝑘−1) 𝑃_𝑖+𝐷_𝑖≤𝐿}=max{𝑘≥0: (𝑘−1) 𝑃_𝑖+𝐷_𝑖≤𝐿}=max{𝑘≥0:𝑘≤(𝐿+𝑃_𝑖−𝐷_𝑖)/𝑃_𝑖 }=:⌊(𝐿+𝑃_𝑖−𝐷_𝑖)/𝑃_𝑖 ⌋

## Slide 7: Processor demand
Checking the schedulability for all time instants is not possible
  Overwhelming complexity
Observation 1: Sufficient to check up to the hyperperiod (schedule repeats itself)
Observation 2: Check only at absolute deadlines. Why?
7
The map is a staircase function with jumps (discontinuities) at absolute deadlines
Time
Demand
supply=time
Notes: Observation 2: Check only at absolute deadlines: Remember: requests become demands at deadline boundaries so the demand makes jumps at absolute deadlines

Observation 2: Check only at absolute deadlines: Remember: requests become demands at deadline boundaries so the demand makes jumps at absolute deadlines
The map t↦⌊(𝑡+𝑃_𝑖−𝐷_𝑖)/𝑃_𝑖 ⌋ is a staircase function with jumps at absolute deadlines 𝑑_(𝑖,𝑘)=(𝑘−1) 𝑃_𝑖+𝐷_𝑖
 ⌊(𝑑_(𝑖,𝑘)+𝑃_𝑖−𝐷_𝑖)/𝑃_𝑖 ⌋=⌊((𝑘−1) 𝑃_𝑖+𝐷_𝑖+𝑃_𝑖−𝐷_𝑖)/𝑃_𝑖 ⌋=⌊𝑘⌋

## Slide 8: Processor demand
Checking the schedulability for at all time instants is not possible
  Overwhelming complexity
Observation 1: Sufficient to check up to the hyperperiod (schedule repeats itself)
Observation 2: Check only at absolute deadlines
Observation 3: If U < 1, the demand is trivially satisfied after some time instant L*
8
Time
Demand
supply=time
L*=?

## Slide 9: Processor demand
Deriving L*
9
Time
Demand
supply=time
L*=?

## Slide 10: Processor demand
Deriving L*
10
Time
Demand
supply=time (t)
L*
Notes: Let . Does the map have a fixed point?
Let (X, d) be a metric space. Then a map T : X → X is called a contraction mapping on X if there exists q ∈ [0, 1) such that
d(T(x),T(y))≤qd(x,y)for all x, y in X.
Banach Fixed Point Theorem. Let (X, d) be a non-empty complete metric space with a contraction mapping T : X → X. Then T admits a unique fixed-point x* in X (i.e. T(x*) = x*).
Well is a contraction mapping when , with and (standard topology on X)
To verify:  take
For L* to be sufficient, must have for all (i.e., that the demand is less than time (taskset feasible) for all times beyond
Since for all , sufficient to show that for all
is increasing, for all  for all
But  for all .
Let 𝐴=∑8_𝑖▒〖(𝑃_𝑖−𝐷_𝑖 ) 𝑈_𝑖 〗. Does the map t↦𝑡𝑈+𝐴 have a fixed point?
Let (X, d) be a metric space. Then a map T : X → X is called a contraction mapping on X if there exists q ∈ [0, 1) such that
d(T(x),T(y))≤qd(x,y)for all x, y in X.
Banach Fixed Point Theorem. Let (X, d) be a non-empty complete metric space with a contraction mapping T : X → X. Then T admits a unique fixed-point x* in X (i.e. T(x*) = x*).
Well 𝑡↦𝑡𝑈+𝐴 is a contraction mapping when 𝑈<1, with 𝑋=[0, ∞) and 𝑑(𝑥,𝑦)=|𝑥−𝑦| (standard topology on X)
To verify: |𝑡𝑈+𝐴 −(𝑡^′ 𝑈+𝐴)|≤𝑈|𝑡−𝑡^′ |  take 𝑞=𝑈∈[0, 1)
For L* to be sufficient, must have 𝑔(𝐿)≤𝐿 for all 𝐿≥𝐿^∗ (i.e., that the demand is less than time (taskset feasible) for all times beyond 𝐿^∗
Since 𝑔(𝐿)≤𝐺(𝐿) for all 𝐿>0, sufficient to show that 𝐺(𝐿)≤𝐿 for all 𝐿≥𝐿^∗
𝐿↦𝐺(𝐿) is increasing, 𝐺(𝐿^∗ )≤𝐺(𝐿) for all 𝐿≥𝐿^∗  𝐺(𝐿^∗ )=𝐿^∗≤𝑮(𝑳)=𝑳𝑼+𝑨 for all 𝐿≥𝐿^∗
But 𝐿^∗=𝐴/(1−𝑈) 𝐴/(1−𝑈)≤𝐿𝑈+𝐴⇒𝐴(1/(1−𝑈)−1)≤𝐿𝑈⇒𝐴𝑈/(1−𝑈)≤𝐿𝑈⇒𝐴≤𝐿−𝐿𝑈⇒𝑳𝑼+𝑨≤𝐿 for all 𝐿≥𝐿^∗.

## Slide 11: Processor demand criterion
Check if
  for all L that are absolute deadlines in the interval [0, L*]
  where
This is an exact test for EDF when relative deadlines are less than task periods
What is the complexity of this test? Is it polynomial-time?
Complexity: Testing constrained-deadine EDF-schedulability is coNP-hard. (Eisenbrand & Rothvoß - SODA’10)
11

## Slide 12: Example using processor demand
Consider the following task set
  T1: (C1=1, P1=3, D1=2)
  T2: (C2=2, P2=7, D2=5.5)
  T3: (C3=2, P3=10, D3=6)
The task set has a hyperperiod of 210
However, we only need to test deadlines up to
U = 86/105 = 0.8190; L* = 8.63
At L = 2:
12

## Slide 13: Example using processor demand
Consider the following task set
  T1: (C1=1, P1=3, D1=2)
  T2: (C2=2, P2=7, D2=5.5)
  T3: (C3=2, P3=10, D3=6)
The task set has a hyperperiod of 210
However, we only need to test deadlines up to
U = 86/105 = 0.8190; L* = 8.63
At L=5.5: (also need to check at L=5; not shown here)
13

## Slide 14: Example using processor demand
Consider the following task set
  T1: (C1=1, P1=3, D1=2)
  T2: (C2=2, P2=7, D2=5.5)
  T3: (C3=2, P3=10, D3=6)
The task set has a hyperperiod of 210
However, we only need to test deadlines up to
U = 86/105 = 0.8190; L* = 8.63
At L=6:
14

## Slide 15: Example using processor demand
Consider the following task set
  T1: (C1=1, P1=3, D1=2)
  T2: (C2=2, P2=7, D2=5.5)
  T3: (C3=2, P3=10, D3=6)
The task set has a hyperperiod of 210
However, we only need to test deadlines up to
U = 86/105 = 0.8190; L* = 8.63
At L=8:
No more absolute deadlines < 8.63. We are done!
15

## Slide 16: Topics covered so far
Periodic Tasks
Deadline=Period
Deadline<Period
Rate Monotonic
EDF
Bounds
Optimality
Result
Bound
Optimality
Result
Deadline Monotonic
EDF
Bound
(Poor)
Per Task
Tests
Simple
Recursive
Processor
Demand
Classical
Hyperbolic
16
Chapter 4 of Buttazzo’s text
Included in the readings

## Slide 17: RM vs. EDF: Judgement Day
Which policy incurs more preemptions?
Which has the edge in implementation simplicity and running time complexity?
How does each behave under transient and permanent overload conditions?
  Is on more predictable than the other when overload happens? In what sense?
Release jitter
17

## Slide 18: Common misconceptions
EDF incurs more preemptions than RM
RM is easier to analyze than EDF
RM introduces less runtime overhead
EDF is not predictable in transient and permanent overloads
RM is more predictable in overload conditions, and causes less jitter in task execution
18
All these statements are either wrong or not precise!
We need to look more carefully into the situation

## Slide 19: Debunking the Myths

## Slide 20: Implementation Cost
For a precise comparison, must distinguish two situations
  Case 1: Scheduler is developed on top of a generic priority-based operating system
  Case 2: Scheduler is developed from scratch
20

## Slide 21: Implementation Cost
Case 1: Scheduler is developed on top of a generic priority-based operating system (limited number of priority levels available)
RM wins!
  Most commercial kernels contain a fixed number or priority levels (typically 256)
Consider the case in which two deadlines and are mapped into two adjacent priority levels
A new periodic instance is released with absolute deadline s.t. .
There is not a priority level that can be selected to map , even when the number of active tasks is less than the number of priority levels in the kernel.
Solution: remap and into two new priority levels that are not consecutive  in worst case, all current deadlines may need to be remapped (high cost)
21

## Slide 22: Implementation Cost
Case 2: Scheduler is developed from scratch
A tie!
RM has a tiny edge: If # of priority levels is low, can split ready queue into separate FIFO queues, one for each priority level  Insertion takes
This is not possible for EDF  number of queues would be too large (e.g., equal to if system time is represented by four byte variables).
22
FIFO Priority 1
FIFO Priority 2
FIFO Priority n
…

## Slide 23: Runtime Cost
EDF incurs less context switches than RM!
But EDF needs to recompute all priorities at job arrivals (not present in RM)
23
RM
EDF

## Slide 24: Context Switching Cost: Interesting Phenomenon
Utilization kept at 0.9 as number of tasks increase
But EDF needs to recompute all priorities at job arrivals (not present in RM)
24
RM
EDF
Notes: For each point in the graph, the average was computed over 1000 independent simulations, each running for 1000 units of time. In each simulation, periods were generated as random variables with uniform distribution in the range of 10 to 100 units of time, whereas execution times were computed to create a total processor utilization U = 0.9.

## Slide 25: Predictability and Stability: Permanent Overload
Permanent Overload 
Behavior of both RM and EDF is predictable in some sense
RM: Might cause complete blocking of lower priority tasks
25
U = 1.25
RM

## Slide 26: Predictability and Stability: Permanent Overload
Permanent Overload 
EDF: Interesting phenomenon happens; Period rescaling
  On the long run, EDF will behave such that it appears that tasks were released at a lower rate 
26

## Slide 27: Predictability and Stability: Permanent Overload
Permanent Overload 
EDF Period rescaling
27
U = 1.25
EDF
Notes: Easy to verify number of activations within first 120 time units:
T1 executes for (arrives) 12 = 120/10 times
T2 arrives 8 = 120/15 times
T3 arrives 5 times =(almost) 120/25 = 4.8

## Slide 28: A deadline miss in EDF can be dangerous
If job misses deadline it executes at a very high priority level (higher than all tasks that have not missed their deadlines)
If late job allowed to continue, will cause other jobs to miss their deadlines!
Need overrun management strategy (application dependent)
  E.g., schedule each late job at a lower priority than jobs that are not late
  Drop late job altogether
28
U = 1.2
After , every job in
both tasks will be late!
J2,1

## Slide 29: Predictability and Stability: Transient Overload
Misconception: In RM, in the presence of transient overload conditions, deadlines are missed predictably, that is, the first tasks that fail are those with the longest period (lowest priority tasks fail first)
EDF: situation is not better than RM!
29
If a task overruns, only the tasks with higher priority than are protected under RM,
but nothing can be ensured for the other tasks.
RM schedule: It’s not that misses its deadline, but rather the higher priority
overrun of 1.5 time units
Notes: transient overload in the first two instances of task τ1 (in the example, the jobs have an overrun of 1.5 time units)

## Slide 30: Handling aperiodic work
EDF has the edge since it has higher utilization
Slack-stealing: If is utilization of periodic work, then the remaining utilization can be used for aperiodic tasks
  Increased utilization given to aperiodic servers (discussed later)
30

## Slide 31: More on RM
Q: Does the utilization bound of RM become 1.0 if all task periods are multiples of the smallest period?
A: No! The correct result is that the utilization bound of RM becomes 1.0 if for every pair of periods, one period in the pair is a multiple of the other.
31

## Slide 32: Lecture summary
Exact test for EDF scheduling (relative deadlines < periods)
Processor demand criterion
RM vs. EDF
32
Giorgio C. Buttazo. Rate monotonic vs. EDF: Judgment day.
Real-Time Systems, 29:5–26. 2005