## Slide 1: 18-349: Introduction to Embedded Real-Time Systems
Anthony Rowe
Electrical and Computer Engineering
Carnegie Mellon University
Lecture 18: Real-Time OS Frameworks

## Slide 2: Administrivia
Lab 3 Due Monday Lab 4 goes out Monday

## Slide 3: Course Feedback
Pace of Course
Lab Difficulty
Lecture Pace
Examinations
Approximate Hours per Week
CONINUE Doing
STOP Doing
START Doing
Other

## Slide 6: Time Spend on Course
14 average

## Slide 7: Things to CONTINUE Doing
4 x Learning about different systems + real world examples
4 x Double office hours / Office hours every day
2 x Hints for Labs during lecture
2 x Interesting Lab Assignments
1 x Open Note Tests
1 x Break in middle of class
1 x Midterm review
1 x Posting slides before class

## Slide 8: Things to STOP Doing
3 x Long Office Hour Wait times
2 x Monday Deadlines
1 x Assignments with lack of resources
1 x No Lab feedback
1 x Buggy Lab Handouts
1 x Vague labs
1 x Lecture material doesn’t match labs
1 x Ignoring Piazza and coming late to office hours
1 x Reading off lectures slides during lecture

## Slide 9: Things to START Doing
11 x More Office hours
4 x Slides before lecture
2 x Improve connection between lectures and labs
1 x Text book
1 x Help with obscure parts of the lab
1 x Respond faster on Piazza
1 x Talk about Virtual Memory
1 x More Lab Feedback
1 x Move deadlines to Wednesday / Friday
1 x Starter code for labs
1 x Late days for labs
1 x Final Project
1 x Lab Recitations

## Slide 10: Other Comments
Lots of variability in lab time
Stop assuming OS (15-410) information is taught in 213
Pick better TAs (ouch!)

## Slide 11: Things we can fix?
Starting Now…
Monday deadlines -> We can shift to Wednesday
TA’s being late / sloppy -> I’ll share ALL of the comments with them
Posting lectures early
Next Time…
Improved lab handouts (will give points for improvements)
Lecture / Lab coupling (I’m working on it…)
Will switch to late days for the labs
Maybe release intermediate solutions (not sure about that yet)

## Slide 12: Why run Linux on it?
Why run Linux on an airplane?
  Right now just for the infotainment system…
Why run Linux on a fighter jet in the future?

## Slide 13: Outline of Lecture
Approaches limiting Real-time and Non-Real-time Task Interactions
  Compliant Kernel Approach
  Dual/Thin Kernel Approach
Approaches that integrate Real-time and Non Real-time tasks
  Core Kernel Approach
  Resource Kernel Approach

## Slide 14: Approaches to Real-Time Linux
Approaches limiting Real-time and Non-Real-time Task Interactions
  Compliant Kernel Approach
    LynxOS/Blue Cat Linux
  Dual Kernel Approach
    RTLinux/RTAI
Approaches that integrate Real-time and Non Real-time tasks
  Core Kernel Approach
    Monta Vista Linux, TimeSys Linux
  Resource Kernel Approach
    Linux/RK

## Slide 15: Linux Internals: Scheduling (1-2)

## Slide 16: Linux Internals: Scheduling (2-2)

## Slide 17: Linux Device Driver

## Slide 18: Linux Networking

## Slide 19: Linux and Real-Time: Traditional Problems
Timer Granularity
  Many real-time tasks are driven by timer interrupts
  In Standard Linux, the timer was set to expire at 10 ms intervals
    Beginning to change with usage of high-resolution timer and timestamp counters
Scheduler Predictability
  The Linux scheduler used to keep tasks in an unsorted list
  Requires a scan of all tasks to make a scheduling decision
  Scales poorly as number of tasks increases, and is especially poor for real-time performance
Various subsystems NOT designed for real-time use
  Network protocol stack
  Filesystem
  Windows manager

## Slide 20: Approaches to Real-Time Linux
Compliant Kernel Approach
Dual Kernel Approach
Core Kernel Approach
Resource Kernel Approach

## Slide 21: Compliant Kernel Approach
Linux Kernel
(Embedded Applications)
Real-Time Kernel
(Real-Time Applications)
Linux System Call API
Linux System Call API
Linux Development Tools
And Environment
Linux Development Tools
And Environment

## Slide 22: Compliant Kernel Approach
Basic Claim
  Linux is defined by its API and not by its internal implementation
  The real-time kernel is a non-Linux kernel
Implications
  No benefits from the Linux kernel
  Not possible to benefit from the Linux kernel evolution
  Not possible to use Linux hardware support
  Not (always) possible to use Linux device drivers

## Slide 23: Compliance
100% Linux API
  Support all of Linux kernel API
Pros
  Any Linux application can run on real-time kernel
    Development can be done on a Linux host, with a rich set of host tools for development
  All Linux libraries are trivially available to run on a real-time kernel
    Third-party software
Cons
  Achieving 100% Linux API is non-trivial
    Consider the amount of effort put into Linux kernel development
  What about cool Linux Kernel features?

## Slide 24: Approaches to Real-Time Linux
Dual Kernel Approach
Compliant Kernel Approach
Core Kernel Approach
Resource Kernel Approach

## Slide 25: Dual Kernel Philosophy
Linux is broken for real-time; Forget it!
Real-Time needs an RTOS
Linux is good for non-real time components

## Slide 26: The Thin (Dual) Kernel Approach
Hardware
Real-Time Kernel (RT-Linux or RTAI)
Real-Time
Task
Real-Time
Task
Real-Time
Task
Linux Kernel
Linux
Process
Linux
Process
User-Level
Kernel-Level
Real-time tasks do NOT use the Linux API or Linux facilities
Failure in any real-time task crashes the entire system

## Slide 27: Dual Kernel Approach
Pros
  Requires little change to Linux Kernel
  Real-Time tasks have tight timing
  Linux apps can run along side RT apps
Cons
  No memory protection on real-time side
  Duplicate Functionality
    Bloat
    Extensibility?
  Sharing of devices between RT side and Linux side
  Starvation of non-RT tasks

## Slide 28: Approaches to Real-Time Linux
Compliant Kernel Approach
Dual Kernel Approach
Core Kernel Approach
Resource Kernel Approach

## Slide 29: Core Kernel Approach
Basic Ideas
  Make the kernel more suitable for real-time
  Ensure that the impact of changes is localized so that
    Kernel upgrades can be easily incorporated
    Kernel reliability and scalability is not compromised
Mechanisms
  Static Configuration
    Can be configured at compile time
  Dynamic Configuration
    Using loadable kernel modules

## Slide 30: Core Kernel Approach

## Slide 31: Core Kernel Approach
Allows the use of most, if not all, existing Linux primitives, applications, and tools.
  Need to avoid primitives that can take extended time in the kernel
Allows the use of most existing device drivers written to support Linux.
  Need to avoid poorly written drivers that unfairly hog system resources
Robustness and Reliability
  Core kernel modifications can affect robustness, but source is available and extensive testing can be done.

## Slide 32: Approaches to Real-Time Linux
Compliant Kernel Approach
Dual Kernel Approach
Core Kernel Approach
Resource Kernel Approach

## Slide 33: Resource Kernel
A Kernel that provides to Applications Timely, Guaranteed, and Enforced access to System Resources
Allows Applications to specify only their Resource Demands, leaving the Kernel to satisfy those Demands using hidden management schemes

## Slide 34: Protection in Resource Kernels
Each application (or a group of collaborating applications) operates in a “virtual machine”:
  a machine which consists of a well-defined and guaranteed portion of system resources
    CPU capacity, disk bandwidth, network bandwidth, and memory resource
Multiple virtual machines can run simultaneously on the same physical machine
  guarantees available to each resource set is valid despite the presence of other (potentially mis-behaving) applications using other resource sets

## Slide 35: Resource Kernel
A Kernel that provides to applications Timely, Guaranteed, and Enforced access to System Resources
Allows Applications to specify only their Resource Demands
  leaving the Kernel to satisfy those Demands using hidden management schemes
Task 1
Task 2
Task 3
Resource Set
Rsv 1
Rsv 2
Rsv 3
Disk
BW
NetBW
CPU
Reservation Parameters
“T”: Period (1/f)
“C”: Execution time within
period
“D”: Deadline within period

## Slide 36: “Resource Kernel” Architecture
Middleware
Services
CPU
Memory
NetBW
Physical
resources
CPU
Memory
NetBW
CPU
NetBW
Memory
CPU
Memory
NetBW
...
Resource
Kernel
RT Filesystem
Publisher/Subscriber
Services
RT-ORB
QoS Mgr
Real-Time
Java
Apps
Real-Time and Multimedia Applications

## Slide 37: Linux Resource Kernel Architecture
Hardware
Resource
Kernel
Linux
Kernel
Linux
Process
Linux
Process
Linux
Process
Kernel
User-Level
LKM

## Slide 38: Reserves and Resource Sets
Reserve
  A Share of a Single Resource
  Temporal Reserves
    Parameters declare Portion and Timeframe of Resource Usage
      E.g., CPU time, link bandwidth, disk bandwidth
  Spatial Reserves
    Amount of space
      E.g., memory pages, network buffers
Resource Set
  A set of resource reserves
  Zero, one or more processes can be bound to a resource set.

## Slide 39: Linux/RK Abstractions
Linux/RK supports several abstractions and primitives for real-time scheduling of processes with real-time and QoS requirements:
Resource reservations with latency guarantees
  CPU cycles
  Network bandwidth
  Disk bandwidth
Support for periodic tasks.
Support for 256 real-time fixed-priority levels.
High-resolution timers and clocks.
Bounding of priority inversion during synchronization operations.
Wiring down of memory pages.

## Slide 40: Reservation Types
Hard Reservations
(guarantees with
No extras even if
resource is idle)
Firm Reservations
(guarantees with
Extras only if no
non-real-time)
Soft Reservations
(guarantees with extras)

## Slide 41: Performance Overhead of Hierarchical Reservations
Linear with the height of the hierarchy
  reservation replenishment and enforcement
Constant
  admission control (only local schedulability analysis)
  scheduling (internal priority mapping and disabling/re-enabling of process eligibility to be scheduled.
Constraints
  reservation period must be greater than twice the parent’s reservation period
Hidden overhead
  Higher degree of interrupts, because of replenishment, enforcement timers going off more frequently.

## Slide 42: Degrees of Temporal Isolation
Different degrees of temporal isolation in the presence of resource-sharing
  Strict Isolation: the timing behavior of an application is not affected by the timing misbehavior of any other application
    RK applications in the absence of logical sharing of resources
  Non-Strict Isolation: traditional priority-driven systems
  Weak Isolation: timing behavior is not affected by the timing mis-behavior of applications with which no logical resources are shared.
App
App
App
App
App
Shared
Rsrc

## Slide 43: Resource-Sharing Protocols in RK
Analogues to Priority Inheritance and Priority Ceiling Protocols in Resource kernels
Temporal isolation can only be weak
  under logical resource-sharing using mutexes and client-server architectures
  timeout and restart schemes may need to be applied.

## Slide 44: Priority Ceiling Protocol Equivalents
Single-Reserve PCP
  Assign one reservation to the logical resource execution
  Very pessimistic allocation is required to maintain PCP semantics’
Multi-Reserve PCP
  Has the same schedulability analysis as traditional PCP
  Requires special support in RK
  Can be applied to client-server models
    Pass client’s reserve to server along with request - charges

## Slide 45: Priority Inheritance Protocol Equivalents
Priority Inheritance (PI)
  Server runs at the priority of the highest priority client waiting for server.
Priority Inheritance with Priority Inversion Enforcement (PIPIE)
  Enforce the duration of priority inversion encountered by any task
    Can never exceed the amount specified at admission control
    Need to track multiple tasks’ priority inversions simultaneously
Reserve Inheritance (RI)
  Server usage is charged to client’s reservation + inherit the highest priority of any client waiting for server
PIPIE + RI
PI
PI+PIE
RI
PI+PIE+RI

## Slide 46: Network and CPU Service Guarantees
Reduction in non-preemptibility
Control of receiver overload (receive -livelock)
Prevention of scheduling disruption
Separation of individual flows and proper resource accounting
Packet scheduling for QoS (Quality of Service) guarantees

## Slide 47: Example System: Small UAV
GPS
1km Low-Speed Radio (802.15.4)
100m High-Speed Radio (802.11) (internal)
Front Facing Camera
Barometric Pressure
Rate Gyro (internal)
3-axis Accelerometer
(internal)
Sonar Ranging
(under)
Digital Compass
Down Facing Camera (under)

## Slide 48: UAV Motivation
Surveillance / Video
Infrastructure Inspection
Search and Rescue
Atmospheric Sensing
Ad-hoc Communication Networks

## Slide 49: 3DR Construction Mapping

## Slide 50: Example System: Small UAV
Sensors
Physical World
Actuators
Compute
GPS, Pressure, Propeller Speed, roll, pitch, yaw, bearing, camera data
Propeller Speed
User
Low-Level Control, Networking, Image Compression, Path Planning

## Slide 51
Linux
468MHz ARM9
128MB RAM
PIC24
40MHz,
4KB RAM
Motors x 4
(local speed controller)
Rate Gyro
Accel.
Ultra-Sound
Serial
Camera PPI x 2
(DMA / Video4Linux)
ROCm Atheros
AR6102G-BM2D b/g Wifi
Expansion Board
ATmega128rfa1
16MHz, 16KB RAM
Serial
GPS
Compass
IR
Pressure
Transducer
Processor
Network Interface

## Slide 52: Main Board
Parrot 6 ARM9
- 468 MHz
ROCm Atheros AR6102G-BM2D b/g Wifi
Micron OGA17 D9HSJ Camera (60FPS, qcif)
Micron 29F1G08AAC Camera

## Slide 53: Sensor Board
PIC24HJ16GP304
- 16 bit, 40 MIPS, 4K RAM, 32K FLASH
2 axis Accelerometer, 3 axis Rate Gyro (Invensense IDG 500), Ultrasound (6 meters)

## Slide 54: Custom Expansion Board
Micro-controller
GPS
Long Range Radio
Sensor Interface

## Slide 55
Navigation Task
Object Detection Task
Video Streaming Task
Actuation Task
Sensor Data Task
Aux Sensor Data
Low-level Flight Control
ftpd
crond
ntpd
Video
network
. . .
RT Prio System
RT Prio User
Linux Non-RT

## Slide 56: Experimental Setup

## Slide 57: Dynamic Workload (Image processing)

## Slide 58: Linux vs RT-Linux
QoS degraded

## Slide 59: Summary
OS Approaches limiting Real-time and Non-Real-time Task Interactions
  Compliant Kernel Approach
  Thin Kernel Approach
OS Approaches that integrate Real-time and Non Real-time tasks
  Core Kernel Approach
  Resource Kernel Approach
Next Lecture: PID Control (guest lecture) + Lab Overview
Notes: 15