## Slide 1: 18-349: Introduction to Embedded Real-Time Systems
Anthony Rowe Steven Aday
Electrical and Computer Engineering
Carnegie Mellon University
Lecture 19: Implementing PID Control

## Slide 2: Overview
Example System
What is a control system?
PID Control
Implementing PID

## Slide 3: Home HVAC

## Slide 4: Printing Press

## Slide 5: Flight Control

## Slide 6: Tokyo Subway (Trains stop at lines)

## Slide 7: Elevators
✔
✗

## Slide 8: Control Systems
We want to control some system
  Called a “Plant”
There is an output value we want to achieve
Output is controlled by an input goal called a “set point”
Controller
Plant
rt
ut
vt+1
Reference Input (set point)

## Slide 9: Control Systems
One option is to create a model of the Plant
A good model predicts output based on input
  ut = F(rt)
Below is an example of an “Open Loop” Controller
Controller
Plant
rt
ut
vt+1
Reference Input (set point)
  ut = F(rt)
  Plant Model
vt

## Slide 10: Motor Example
You want to control some motor
You realize that the speed is related to the input voltage…
Motor Model: vt+1 = 0.7 vt + 0.5 ut + dt
  dt is some sort of disturbance in the plant
Control Function: F(rt) = P rt
Controller
Plant
rt
ut
vt+1
Reference Input (set point)
  ut = F(rt)
  Plant Model
vt
Desired Speed
Voltage
Motor Speed

## Slide 11: Driving a Motor
Motors draw lots of current
PWM signal used to apply a virtual voltage
H-Bridge (actuator lecture)
GPIO / PWM
GPIO / PWM
Microcontroller

## Slide 12: Motor Example
Control Function: F(rt) = P rt
What should P be?
In steady state we measure:
  With ut = 3000 mV we get vt = 5000 rpm
  With ut = 600 mV we get vt = 1000 rpm
  It seems like 1 volt corresponds to a 1666 rpm change?
Controller
Plant
rt
ut
vt+1
Reference Input (set point)
  ut = F(rt)
  Plant Model
vt
Desired Speed
Voltage
Motor Speed

## Slide 13: Motor Example
Lets sanity check our model…
Motor Model: vt+1 = 0.7 vt + 0.5 ut + dt
    With ut = 600 mV we get vt = 1000 rpm
Steady State (at 600mV)
  assume Vt = 1000 rpm,
  Vt+1 = 0.7 *1000 + 0.5 600
  Vt+1 = 1000
Steady State (at 3000mV)
  assume Vt = 5000 rpm,
  Vt+1 = 0.7 *5000 + 0.5 3000
  Vt+1 = 5000

## Slide 14: Problems with Open Loop Systems
They are “flying” blind
  Dead reckoning
Can not respond to disturbances
  Extra friction etc.
Controller can not adjust to different plants
Models are probably not linear and could be impossible to derive
Controller
Plant
rt
ut
vt+1
Reference Input (set point)
  ut = F(rt)
  Plant Model
vt
Desired Speed
Voltage
Motor Speed

## Slide 15: Open Loop Motor P-Control - Nominal

## Slide 16: Open Loop Motor Control – Kf = 1.2

## Slide 17: Open Loop Motor Control – +0.5 Nm disturbance

## Slide 18: Close Loop Systems
Add feedback so the controller knows result of inputs
If we can measure the difference between the set point and the output we can compute error
Controller
Plant
rt
ut
vt+1
Reference Input (set point)
  ut = F(rt)
  Plant Model
vt
  Sensor
et
Error: et = rt - vt

## Slide 19: Sensing motor speed (1-3)
Often use optical encoders

## Slide 20: Sensing motor speed (2-3)
Quadrature Encoding
  Capture counts and direction

## Slide 21: Sensing motor speed (3-3)
Typical circuit
  Connect to GPIO interrupts on an MCU
MCU
Quadrature to
Up / Down Decoder

## Slide 22: Closed Loop Motor Control – Nominal Bang-Bang

## Slide 23: Proportional Control
Simplest controller
F(et) = Kp (et)
  Look at the error value
  Increase the input as a linear proportional function to the error
Controller
Plant
rt
ut
vt+1
Reference Input (set point)
  ut = F(rt)
  Plant Model
vt
  Sensor
et
Error: et = rt - vt

## Slide 24: Motor Example (Proportional)
With load on the motor we now see:
  3000mV is giving a speed of 3000rpm
  According to the model it should give 5000rpm!
  Error = 5000-3000 = 2000 rpm
Lets boost the voltage by some proportion Kp of the error
  Assume Kp = 0.5
  That would mean our new input voltage would be:
    3000mV + 0.5 * 2000 = 4000mV
  Adding more voltage should certainly help the motor go faster...

## Slide 25: Oscillation
When your error is high, your added input is high
You can then overshoot and oscillate

## Slide 26: Closed Loop Motor Control – Nominal P-Control, Kp = 10

## Slide 27: Closed Loop Motor Control –P-Control, Kp = 10, Disturbance at t=5

## Slide 28: Adding a Derivative Term
What if we look at the rate of change as we approach our target?
  If too slow, increase the control input
  If too fast, decrease the control input
F(et) = Kp (et) + Kd (et – et-1 )
This derivative term Kd decreases oscillation
  It Dampens the control response
Controller
Plant
rt
ut
vt+1
  ut = F(rt)
  Plant Model
vt
  Sensor
et

## Slide 29: Proportional Derivative (PD) Controller
Over Damped versus Under Damped

## Slide 30: Closed Loop Motor Control –PD Control, Kp = 10, Kd = 5

## Slide 31: Closed Loop Motor Control –PD Control, Kp = 10, Kd = 2, disturbed

## Slide 32: Long-term Cumulative Error
What if you can’t reach your target because of constant error?
  For the motor it could be wind, a hill, too much friction etc…

## Slide 33: Integral Term
If we sum our error over time, we might see that we need a little extra boost to meet our goal
Ki will provide an input based on the integrated error over time
F(et) = Kp(et) + Ki(e0 + e1 + e2 + … + et-1 )
Controller
Plant
rt
ut
vt+1
  ut = F(rt)
  Plant Model
vt
  Sensor
et

## Slide 34: Adding in the Integral Term
In the case of the motor we would slowly add more voltage depending on the long term error
Slowly Increase the input based on long-term Error

## Slide 35: Closed Loop Motor Control –PID Control, Ki = 5, disturbed

## Slide 36: Summary of PID Controller
F(et) = Kp (et) + Kd (et – et-1 ) + Ki (e0 + e1 + … + et-1)

## Slide 37: PID Implementation
typedef struct {
double dState; // Last position input
double iState; // Integrator state
double iMax, iMin; // Maximum and minimum allowable integrator state
double iGain, // integral gain
pGain, // proportional gain
dGain; // derivative gain
} SPid;
double UpdatePID(SPid * pid, double error, double position) {
double pTerm, dTerm, iTerm;
pTerm = pid->pGain * error;
// calculate the proportional term
// calculate the integral state with appropriate limiting
pid->iState += error;
if (pid->iState > pid->iMax) pid->iState = pid->iMax;
else if (pid->iState < pid->iMin) pid->iState = pid->iMin;
iTerm = pid->iGain * iState; // calculate the integral term
dTerm = pid->dGain * (position - pid->dState); pid->dState = position;
return pTerm + iTerm - dTerm;
}

## Slide 38: PID Implementation
typedef struct {
double dState; // Last position input
double iState; // Integrator state
double iMax, iMin; // Maximum and minimum allowable integrator state
double iGain, // integral gain
pGain, // proportional gain
dGain; // derivative gain
} SPid;
double UpdatePID(SPid * pid, double error, double position) {
double pTerm, dTerm, iTerm;
pTerm = pid->pGain * error;
// calculate the proportional term
// calculate the integral state with appropriate limiting
pid->iState += error;
if (pid->iState > pid->iMax) pid->iState = pid->iMax;
else if (pid->iState < pid->iMin) pid->iState = pid->iMin;
iTerm = pid->iGain * iState; // calculate the integral term
dTerm = pid->dGain * (position - pid->dState); pid->dState = position;
return pTerm + iTerm - dTerm;
}
typedef struct {
double dState; // Last position input
double iState; // Integrator state
double iMax, iMin; // Maximum and minimum
// allowable integrator state
double iGain, // integral gain
pGain, // proportional gain
dGain; // derivative gain
} SPid;
double UpdatePID(SPid * pid, double error, double position)
pTerm = pid->pGain * error;
// calculate the proportional term
// calculate the integral state with appropriate limiting
pid->iState += error;
if (pid->iState > pid->iMax) pid->iState = pid->iMax;
else if (pid->iState < pid->iMin) pid->iState = pid->iMin;
iTerm = pid->iGain * iState; // calculate the integral term
dTerm = pid->dGain * (position - pid->dState);
pid->dState = position;
return pTerm + iTerm - dTerm;

## Slide 39: How do we pick Kp, Ki, and Kd?
Stability
  We want the error to eventually converge to 0
Performance Metrics
  Rise time / Response: How long does it take to get to 10% of the final value?
  Peak time: Time to reach first peak
  Overshoot: Amount in excess of final value
  Settling Time: Time before output settles to within 1% of final value

## Slide 40: Tuning a PID Controller
A search in 3 Dimensions
ALWAYS instrument system to collect response graphs
  If you can’t measure it, you can’t tune it!
Build an Interactive Interface
  Set P,I and D terms from a terminal interface quickly
Heuristic Procedure 1 (leading with the D term):
  Step 1: Set Kp to small value, Kd and Ki to 0
  Step 2: Increasing Kd until oscillation, then decrease by factor of 2-4
  Step 3: Increase Kp until oscillation or overshoot, decrease by 2-4x
  Step 4: Increase Ki until oscillation or overshoot
  Step 5: Is it okay? If not, go to Step 2.

## Slide 41: Tuning a PID Controller
Heuristic Procedure 2 (leading with the P term):
  Step 1: Set Kd and Ki to 0
  Step 2: Increasing Kp until oscillation, then decrease by factor of 2-4
  Step 3: Increase Ki until loss of stability, then dial it back
  Step 4: Increase Kd to react against disturbance as needed
  Step 5: Is it okay? If not, go to Step 2.

## Slide 42: Other Considerations
Sampling Rate
  1/10 to 1/100 the settling time
  Faster usually makes things easier

## Slide 43: Industrial Controllers

## Slide 44: Conclusions
PID control is used by 90% of control systems
Its fun and easy
Every embedded developer should know the basics so you can control stuff
Next Class: Course Wrap-up