## Slide 1: 18-349: Introduction to Embedded Real-Time Systems
Anthony Rowe
Electrical and Computer Engineering
Carnegie Mellon University
Lecture 21: Wireless Communication

## Slide 2: Administrivia
Lab 4 due next Wednesday (Dec. 7th)
Redemption Lab due (Dec. 12th)
Final (Friday Dec. 16th 8:30-11:30am)

## Slide 3: Overview
Motivation for Wireless
Wireless Challenges
Wireless MAC Principles
Example Technologies
  IrDA
  NFC
  802.15.4
  Zigbee
  Bluetooth
  WiFi
  LTE
  LP-WAN

## Slide 4: Why Wireless Communication?
Reduced Installation cost / weight
  Airplanes / cars / building sensors etc
High Mobility
  Cellphones, wearables, etc
Reconfigurable / Fault Tolerant
  Double-edged sword

## Slide 5: Wireless Challenges
Data Rate / Packet Loss (Physical Layer Issues)
  Air is not as good of a medium as copper
  Slow Fading / Fast Fading
Single Duplex Channel
  Difficult to transmit / receive on same frequency
Broadcast Domain (collisions)
  Hidden Terminal Problem
  Exposed Terminal Problem
  Near-Far Problem

## Slide 6: Hidden Terminal
Node A and Node C transmit to Node B at the same time…
a
b
c
X

## Slide 7: Exposed Terminal
Node B and Node C try sending to Node A and Node D respectively
Node B overhears Node C’s transmission and doesn’t send to avoid a collision…
Decrease in network throughput
a
b
c
X
d

## Slide 8: Near-Far Problem
Node A and Node B often get a “fair” share of bandwidth
Since Node B is much slower it decreases Node A’s capacity
ap
a
b
54 Mbps
1 Mbps

## Slide 9: Wireless Topologies

## Slide 10: Wireless Channel Dimensions
Time
Frequency
Coding
Space (Directional Antennas)
space
space
space

## Slide 11: ALOHA
1
2
3
3
2
Time
Collision
Retransmission
Retransmission
Node 1 Packet
Collision mechanism in ALOHA
Waiting a random time
Node 2 Packet
Node 3 Packet

## Slide 12: Carrier Sense Multiple Access (CSMA)
1
2
3
Time
Collision
4
Node 4 sense
Delay
5
Node 5 sense
Delay
Node 1 Packet
Node 2 Packet
Node 3 Packet

## Slide 13: What about power?
Typical Low-Power Radio Power States (802.15.4)
  Idle: 426 µA
  Power Down: 20 µA
  Voltage Regulator Off: 0.2 µA
  TX: 17.4mA
  RX: 18.8mA
* All currents at 3 volts
Sleep
Idle
TX
RX
860 μS
2 μS

## Slide 14: Radio + CPU Power
Active: 7 mA  17 days
Active + TX: 24.4 mA  4.9 days
Active + RX: 28.8 mA  4.6 days
Idle: 2 mA  60 days
Sleep: 70 µA  4.68 yrs!
2,870 mAH (@ 25ma) 1.5v x 2 (series)

## Slide 15: Low Power Listen (LPL)
Check Interval
Sampling Interval
Radio RX
Radio TX
Radio RX
Radio TX
A
B

## Slide 16: LPL-CSMA
Radio TX
Radio RX
Radio TX
Radio RX
Listen Frequently
Transmit Longer

## Slide 17: LPL-CSMA
Optimal Check Interval (ms)
Sampling Interval (min)
Check Interval (ms)
Life (yrs)
20 min
30 min
40 min
60 min
Multiple Sampling Intervals

## Slide 18: TDMA-Based Approach
Time-Sync Cycle
Sync Pulse
Frame (32 per TDMA Cycle)
Scheduled Slots
Contention Slots
32 Slots Per Frame
Sync Pulse

## Slide 19: TDMA Graph Coloring
“Color” Topology Graph to Avoid Collisions
Each color represents a TDMA slot
a
b
d
c
d
e
f
Gateway
a
b
d
c
d
e
f
a
b
c
TX
RX
TX
RX
TX
RX
TDMA Frame

## Slide 20: Wireless Technologies
How do you integrate wireless into an embedded system?
What are the tradeoffs?
Common Technologies:
  IrDA
  NFC
  802.15.4
  Zigbee
  Bluetooth
  Low-Power Wide Area Networks
  WiFi
  LTE

## Slide 21: Communication Trade-offs
Performance
(bandwidth, range, etc)
Cost
($$$, power, complexity, etc)
UART, I2C, SPI
802.15.4, BLE, CAN
WiFi, Celluar, Ethernet

## Slide 22: ISM Band
Industrial, Scientific and Medical (ISM) radio bands
Unlicensed Spread Spectrum
Multiple frequencies: 900MHz, 2.4GHz, 5.8Ghz, …
A few bands are accepted world-wide…

## Slide 23: IrDA
Uses Infrared light
Appliance Remote Control
Super Cheap / Easy to Build
Typically 9600 baud (up to Mega Baud)

## Slide 24: IrDA Transceiver

## Slide 25: IrDA Modulation

## Slide 26: Near-Field Communication (NFC)
Used in mobile payment
Short Range
RF inductive coupling
  Send power for receiver
Low-Cost Receiver
Expensive Transmitter

## Slide 27: 802.15.4
Physical Layer for Zigbee, ISA100.11a, WirelessHART, 6LoWPAN
Mesh Wireless
2.4GHz, 16 channels, 250 kbits/s
Comparison to WiFi
  Similar range
  Lower data rate
  Lower power

## Slide 28: 802.15.4
Modules with Serial AT command Interface
SoC with Microcontroller
Approximate Energy
1.8v
20mA RX
20mA TX
4ms max packet time

## Slide 29: Zigbee
Built on 802.15.4, but adds:
- Routing
- Security
- Duty-cycling
- Application Specs

## Slide 30: Bluetooth
Designed as Cable Replacement
2.4 GHz, 10-60m range, 3 Mbit/sec
Version 1-2
  Big, slow, complicated
Version 3-4
  24 Mbits/s
  BLE (bluetooth low energy)

## Slide 31: Bluetooth Low-Energy
TI CC2540 BLE chipset

## Slide 32: WiFi
802.11 a,b,g,n,p,ac,…
Typically 2.4 and 5 GHz
100m range and up to 600 Mbit/s
60GHz 802.11ad 7 Gbit/s
High-speed Ethernet replacement
Power hungry (can be duty-cycled)

## Slide 33: WiFi Interfacing
TI CC3000 (SPI)
Electric IMP
(cloud solution)
Xbee Wifi Module (UART)
Approximate Energy
3v
100mA RX
150mA TX
<4ms MTU packet time
ESP8266 (SPI)

## Slide 34: GSM / LTE
Cellular is pervasive
  Good for remote monitoring
Can be expensive for a single device
  Telemetry plans are available

## Slide 35: GSM / LTE options
Approximate Energy
3.3v
350mA RX
2000mA TX
Spreadtrum SM5100B (UART)

## Slide 36: Low-Power Wide Area Networks (LP-WAN)
Pervasive network for IoT devices
  Battery powered client devices
  Easy-to-use and secure
  Large-Scale 10K+ devices
  Open to CMU community…
Why LP-WAN?
  Cellular solution are expensive in terms of both hardware and contracts…
  Not optimized for long-term battery-operated devices…
  Coverage of reomte areas

## Slide 37: Why now?
WiFi and LTE have pushed radio performance…
  Great sensitivity
  Great power envelope
  Advanced modulation at a low cost
LP-WAN Explosion
  Narrowband radios: LoRa, LTE-MTC, SigFox...
  We are borrowing from all of the technologies...
Trade-off speed for range and power
  WiFi: 10-300 Mbps at 100m
  LoRa: 0.3-50kbps at 15km (2km urban)

## Slide 38: Wireless Space for IoT (1-2)

## Slide 39: Wireless Space for IoT (2-2)

## Slide 40: LP-WAN Technologies
LoRA
  <1GHz Chirp Spread Spectrum
  “Open”
  Semtech chipset
LTE-MTC
  <1GHz Narrow Band LTE
SigFox
  <1GHz power amplified 802.15.45
  Proprietary

## Slide 41: The OpenChirp Project Open and Secure Low-Power Wide Area Networking

## Slide 42: Concentrator Hardware Prototype
PoE Supply
Low Cost SDR
GPS
Embedded Linux
Custom LoRa Gateway (40K+ clients per gw)

## Slide 43: Concentrators
Independent 1-λ separated 5.5dBi 902MHz ~ 928MHz antennas with grounding rod (custom assembly)

## Slide 44: CMU Campus Locations

## Slide 45: Craig Street Aggregator

## Slide 46: Tepper Aggregator

## Slide 47: Serious Range…
Rooftop to Indoor Packet Reception at 1.7miles!

## Slide 48: Commercial LoRa Clients
Many commercial devices already coming onto the market…
Street Sensor
Smoke Detector
Citizens Science Kits
Temperature Sensor
Key Fob

## Slide 49: LoRa Bug Custom Client
Sensor Board: Light, Temperature, Accelerometer, Magnetometer, Rate Gyro, Humidity, Water Contact, Pressure, Audio, PIR motion
SX1276
LoRa Radio
TI CC2650 ARM M3
BLE + 802.15.4
FireFly
Sensor Header
USB

## Slide 50: OpenChirp Concept
Step 1: Setup an account
Step 2: Grab a LoRa Device
Step 3: Configure Devices
Step 4: Deploy the device
Sounds easy, but there is a lot that needs to be done under the hood…
Step 5: Manage Devices
ReST
CoAP
MQTT
AMPQ
XMPP

## Slide 51: Conclusions
Lots of activity in the wireless space right now
Many options for integration into embedded systems
  Many trade-offs between power / cost / complexity
Next Class: Embedded Security