## Slide 1: 18-349: Introduction to Embedded Real-Time Systems
Anthony Rowe
Electrical and Computer Engineering
Carnegie Mellon University
Lecture 8: ADC and DAC*
* Slides based off of Prabal Dutta at University of Michigan’s embedded course.

## Slide 2: Administrivia
Lab 1
  1 weeks away!

## Slide 3: Last Lecture
ARM optimizations

## Slide 4: Lecture Overview
Analog to Digital Converters
Digital to Analog Converters

## Slide 5: We live in an analog world
Everything in the physical world is an analog signal
  Sound, light, temperature, pressure
Need to convert into electrical signals
  Transducers: converts one type of energy to another
    Electro-mechanical, Photonic, Electrical, …
  Examples
    Microphone/speaker
    Thermocouples
    Accelerometers

## Slide 6: Transducers convert one form of energy into another
Transducers
  Allow us to convert physical phenomena to a voltage potential in a well-defined way.
A transducer is a device that converts one type of energy to another. The conversion can be to/from
electrical, electro-mechanical, electromagnetic, photonic, photovoltaic, or any other form of energy.
While the term transducer commonly implies use as a sensor/detector, any device which converts energy
can be considered a transducer. – Wikipedia.

## Slide 7: Going from analog to digital
What we want
How we have to get there
Software
Sensor
ADC
Physical
Phenomena
Voltage or
Current
ADC Counts
Engineering Units
Physical
Phenomena
Engineering Units

## Slide 8: Representing an analog signal digitally
How do we represent an analog signal?
  As a time series of discrete values
   On MCU: read the ADC data register periodically
V
Counts
8

## Slide 9: Choosing the horizontal range
What do the sample values represent?
  Some fraction within the range of values
   What range to use?
Range Too Small
Range Too Big
Ideal Range
9

## Slide 10: Choosing the horizontal granularity
Resolution
  Number of discrete values that represent a range of analog values
  MSP430: 12-bit ADC
    4096 values
    Range / 4096 = Step
  Larger range  less information
Quantization Error
  How far off discrete value is from actual
  ½ LSB  Range / 8192
  Larger range  larger error
10

## Slide 11: Choosing the sample rate
What sample rate do we need?
  Too little: we can’t reconstruct the signal we care about
  Too much: waste computation, energy, resources
11

## Slide 12: Shannon-Nyquist sampling theorem
If a continuous-time signal contains no frequencies higher than , it can be completely determined by discrete samples taken at a rate:
Example:
  Humans can process audio signals 20 Hz – 20 KHz
  Audio CDs: sampled at 44.1 KHz
12

## Slide 13: Converting between voltages, ADC counts, and engineering units
Converting: ADC counts  Voltage
Converting: Voltage  Engineering Units
13

## Slide 14: A note about sampling and arithmetic*
Converting values in 16-bit MCUs
  vtemp = adccount/4095 * 1.5;
  tempc = (vtemp-0.986)/0.00355;
   vtemp = 0! Not what you intended
   tempc = -277 C
Fixed point operations
  Need to worry about underflow and overflow
Floating point operations
  They can be costly on the node
14
Notes: $ cat arithmetic.c
#include <stdio.h>
int main() {
int adccount = 2048;
float vtemp;
float tempc;
vtemp = adccount/4095 * 1.5;
tempc = (vtemp-0.986)/0.00355;
printf("vtemp: %f\n", vtemp);
printf("tempc: %f\n", tempc);
}
$ gcc arithmetic.c
$ ./a.out
vtemp: 0.000000
tempc: -277.746490

## Slide 15: Use anti-aliasing filters on ADC inputs to ensure that Shannon-Nyquist is satisfied
Aliasing
  Different frequencies are indistinguishable when they are sampled.
Condition the input signal using a low-pass filter
  Removes high-frequency components
  (a.k.a. anti-aliasing filter)
15

## Slide 16: Designing the anti-aliasing filter
Note
  w is in radians
  w = 2pf
Exercise: Say you want the half-power point to be at 30Hz and you have a 0.1 μF capacitor. How big of a resistor should you use?
16
Notes: 53K
2*pi*f = 1 / (R * C)
2*pi*30 = 1 / ( R * .1e-6)
R = 53051

## Slide 17: Do I really need to condition my input signal?
Short answer: Yes.
Longer answer: Yes, but sometimes it’s already done for you.
  Many (most?) ADCs have a pretty good analog filter built in.
  Those filters typically have a cut-off frequency just above ½ their maximum sampling rate.
    Which is great if you are using the maximum sampling rate, less useful if you are sampling at a slower rate.
17

## Slide 18: Can use dithering to deal with quantization
Dithering
  Quantization errors can result in large-scale patterns that don’t accurately describe the analog signal
  Oversample and dither
  Introduce random (white) noise to randomize the quantization error.
Direct Samples
Dithered Samples
18

## Slide 19: Single-Ended vs Differential
Rail-to-Rail????

## Slide 20: ADS1015 (our friend from lab 1)

## Slide 21: Lab 1 Board

## Slide 22: Microphone

## Slide 23: ADS1015

## Slide 24: ADS1015

## Slide 25: ADS1015 - Reg Maps (RTM)

## Slide 26: ADS1015 - PGA
Note the programmable gain amplifier (PGA)…

## Slide 27: ADS1015 – I2C

## Slide 28: Analog to Digital Converter (ADC)
FLASH (parallel) ADC
RAMP Counter ADC
Successive Approximation ADC
Single Slope ADC
Sigma-Delta ADC
Digital World
Real World
(Voltage)
28

## Slide 29: FLASH ADC
+Simple and Fast
-Requires many components
(8 bit requires 255 compares!)
29

## Slide 30: RAMP ADC
Increase value until comparison found
Very slow…
30

## Slide 31: Successive Approximation ADC
Check MSB -> LSB comparisons
Finds value in N cycles for N bits
Most common ADC architecture
31

## Slide 32: Single-Slope ADC
Similar to a RAMP circuit, but uses a time-based integrator to produce voltage
Vref
time
32

## Slide 33: Sigma-Delta ADC
Similar to ramp ADC, but controlled by 1-bit DAC
Simple Analog w/ complex digital makes it cheap to manufacture
Accuracy and update rate are good
33

## Slide 34: Digital to Analog Converter (DAC)
PWM DAC
Binary-scaled DAC
Voltage Divider DAC
Digital World
Real World
(Voltage)
34

## Slide 35: PWM DAC
35

## Slide 36: Binary-scaled DAC Architecture
36

## Slide 37: Voltage Divider DAC Architecture
Fast
Size (transistors, switches)?
Accuracy?
Monotonicity?
37

## Slide 38: Ladder DAC
38

## Slide 39: DAC output signal conditioning
Often use a low-pass filter
May need a unity gain op amp for drive strength
39

## Slide 40: Amplifiers (quick thoughts)
GPIO
  Current limit of 20mA
DAC
  Even less
Controlling a relay
40

## Slide 41: Summary
Analog-to-digital Converters (ADC)
Digital-to-analog Converters (DAC)
Next: Sensors and Actuators