## Slide 1: 18-349: Introduction to Embedded Real-Time Systems
Anthony Rowe
Electrical and Computer Engineering
Carnegie Mellon University
Lecture 9: Transducers

## Slide 2: Administrivia
Lab 1
  Due Monday
Final Exam
  Date: Thursday December 15, 2016
  Time: 5:30pm-8:30pm
  Location: TBA
Late Policy
Style Points

## Slide 3: Late Policy
You can turn in one lab at up to 85% of the original value before December 12th
Labs 0-3 build off of each other (Lab 4 not as much)
More practically, this means that you can utilize time at the start of a new lab to finish the previous lab if you did not complete it. Use as many days as you want until December 12th, but keep in mind you need to finish the newly released lab as well.

## Slide 4: Coding Style
Good Comments
Good Use of Whitespace
Line Length (80 characters)
Good Variable Names
Magic Numbers
No “Dead Code”
Modularity of Code
Failure Conditions / Error Checking
Proper Memory Handling
Consistency (stick with one style across the entire file)
If in doubt, refer to: https://www.cs.cmu.edu/~213/codeStyle.html

## Slide 5: Last Lecture
Analog to Digital Converters
Digital to Analog Converters

## Slide 6: Lecture Overview
Sensors
Noise
  Time Domain vs. Frequency Domain
  Filtering
Actuators

## Slide 7: What is a sensor?
A sensor converts a physical phenomenon into an electrical signal
  Physical  Electrical
An actuator does the opposite
  Electrical  Physical
A transducer is a sensor, actuator, or both

## Slide 8: Physical Phenomena
Human Related Senses
  Light, Sound, Taste, Smell, Touch, Balance, Temperature, Time
Non-Human Senses
  Magnetoreception, Electroreception, Voltage, Current, Capacitance, Resistance

## Slide 9: Types of Sensing
Passive Sensing (self-generating)
  Sensors that collect energy that is naturally available
  Does not interfere with the environment
  Examples: Thermocouple, photodiode, piezoelectrics
Active Sensing
  Sensors that provide their own “illumination”
  Can sense anytime (for example no need to wait for sunlight)
  Require additional energy
  Examples: RADAR, Microwave Motion, SONAR, RTD

## Slide 10: Example Sensors
Property | Sensor | Active/Passive | Output
Temperature | Thermocouple | Passive | Voltage
 | Silicon | Active | Voltage/Current
 | RTD (resistance temperature detector) | Active | Resistance
 | Thermistor | Active | Resistance
Force/Pressure | Strain Gage | Active | Resistance
 | Piezoelectric | Passive | Voltage
Acceleration | Accelerometer | Active | Capacitance
Position | LVDT (linear variable differential transformer) | Active | AC Voltage
 | IR distance | Active | Voltage / Digital
Light Intensity | Photodiode | Passive | Current
 | CMOS Camera | Passive | Digital

## Slide 11: Basic Sensing Components
Sensor
Amp.
ADC
Micro-controller
Impedance Matched Signals

## Slide 12: Calibration
The relationship between the physical measurement variable (X) and the signal variable (S)

## Slide 13: Sensor Parameters
Range
  Lower and upper limits
Resolution
  Minimum difference between two measurements
  Example: 8bit ADC with 5 volt input
Dynamic Range
  Used to measure spread between lower and upper limits
  Usually a ratio in decibels (dB)
    Dynamic Range = 10 log (Upper Limit / Lower Limit)
Notes: 5Volts / 256 = 0.02 volts

## Slide 14: Sensor Parameters
Sensitivity
  Slope of calibration curve
Linearity
  Closeness of the calibration curve to a specific straight line (least squares fit)
Monotonicity
  A curve where the dependent variable always increases or decreases with changes in the independent variable
Hysteresis
  Difference between two output values given the same input value depending on the trajectory of the sensor

## Slide 15: Sensor Parameters
Bandwidth or Frequency
  The speed at which a sensor can provide a stream of meaningful readings

## Slide 16: Accuracy, discrimination and precision
Accuracy
  Ability to report values close to the TRUE value
Discrimination
  Minimal input change required to produce detectable output change
Precision
  Repeatability of the reading

## Slide 17: Shooter Example
Shooter #1
Shooter #2
Discrimination
Size of the hole produced by a shot
Which shooter is more accurate?
Which shooter is more precise?
Notes: Shooter 2 is more accurate
Shooter 1 is more precise

## Slide 18: Errors – What can go wrong?
Systematic
  Interfering inputs or modifying variables
  Drift (mechanical stress)
  Measurement process changed (new loading)
  Transmission process changed (attenuation)
Random
  Noise

## Slide 19: Sensor Parameters (Summary)
Parameter | Description
Transfer Function | Mapping between physical input signal and the electrical output signal
Sensitivity | Change in signal vs change in physical input
Dynamic Range | Range over which physical values are differentiated
Accuracy | Largest expected error between reported and true value
Hysteresis | Lag between true and sensed values
Temperature Coefficient | Change due to temperature (not real physical change)
Linearity | Delta from transfer function and a linear equation
Noise | Electronic fluctuations in signal
Resolution | Min detectable signal fluctuation
Bandwidth | Difference in frequency range between finite response times (activation) and the signal decay times (deactivation)

## Slide 20: Reading Sensors
Resistive (R)
Capacitive (C)
Inductive (L)

## Slide 21: Resistive Sensor
Voltage Divider
Wheatstone Bridge
Rs
R1
Rs
Examples: light, temperature

## Slide 22: Capacitance
Capacitance to Frequency Converter
Use Timers / Capture Compare Units
Examples: humidity, touch

## Slide 23: Inductive Sensors
Examples: precise position sensor LVDT

## Slide 24: Electro-Chemical
Examples: Gas sensors

## Slide 25: Micro-Electro Mechanical Sensors (MEMS)
Examples: Accelerometer, rate gyro

## Slide 26: Digital Sensors
Sensor / Amp. / ADC / microcontroller are internal
Example: BMP085 Pressure Sensor

## Slide 27: Sharp IR Sensor (Active Sensor)

## Slide 28: Sharp IR Sensor
Convex lens
Concave lens
CMOS Line Sensor
IR LED

## Slide 29: Common Sensors

## Slide 30: What is noise?
Unwanted fluctuation in a “reading”
“Electrical Noise”
  Electrical signals that make it more difficult to detect or process a signal of interest
  Limits sensors, high-speed circuits and RF receivers

## Slide 31: Where does noise come from?
External Sources
  Crosstalk, Motors, lightning bolts, surges etc
Material Properties
  Thermal excitement, impurities in a conductive channel, semiconductor base currents, …

## Slide 32: How is noise typically quantified?
TLC2201 Op-Amp Noise Specification in data sheet
“Noise Floor”
  Noise level when all inputs are turned off and all outputs are correctly terminated

## Slide 33: Sampling Rates and Resolution
Analog waveforms are continuous
ADC has a fixed frequency (x-axis)
ADC has a fixed resolution (y-axis)
Nyquist’s Rule: sample at 2x the max freq. of signal

## Slide 34: Time and Frequency
Time Domain
Frequency Domain
Fourier
Transform
Inverse Fourier
Transform

## Slide 35: Time and Frequency

## Slide 36: Square Wave Example

## Slide 37: Fast Fourier Transform
Fast Fourier Transform (FFT)
  Optimized version of the Discrete Fourier Transform (DFT)
  Works on buffers with a power of two length (i.e. 512, 1024, 2048)
int time_s = [ 3, 4, 8, 8, 4, 2, 1, 2, 3, 4, 5, 7, 8, 8, 6, 4, 3, 1, 1 ] ;
int freq_s [16];
int freq_s = [ 1, 1, 2, 1, 8, 8, 1, 2, 1, 2, 1, 2, 1, 1, 2, 1 ];
Frequency (Hz)
Amplitude
status = fft ( time_s, freq_s );
Time (samples)
Amplitude

## Slide 38: Digital Filtering
FFT
Noise?
Low Pass Filter
Zero out upper frequency values…
iFFT

## Slide 39: Audio Equalizer

## Slide 40: Lab 2: Guitar Tuner
Note | Frequency
E | 82.4
A | 110.00
D | 146.83
G | 196.00
B | 246.94
E | 329.63
F=84
F=85
F=84
F=83 …
Periodic sampling
FFT
Peak Detection
Serial Output
Interrupts and SWI for periodic sampling

## Slide 41: What is an Actuator?
Something that converts energy into motion (or applies a force)
Electrical
  Motors, Solenoid, Piezoelectric, Electroactive polymers, Speakers, heating coil
Chemical
  Animal Muscle, Combustion Engine
Hydraulics
  Fluid Pressure

## Slide 42: Motor Controller
Motor
H-Bridge
Encoder
Controller (PID)
Output
Sensing
Feedback
Weak Signal
Amplified Signal

## Slide 43: Motors
AC / DC Motor
  Magnetic, Electrostatic
Stepper Motor
  Brushless motor that moves discrete steps
  Can be very accurate without sensing
Servo Motor
  Motor with built-in sensing to hold set positions
  Usually does not rotate 360 degrees

## Slide 44: Encoder
00
01
11
10
Grey Code State Machine

## Slide 45: H-Bridge Circuit

## Slide 46: Servo

## Slide 47: Solenoid
Magnet pulling on spring-loaded linear actuator
Used in door locks and valves

## Slide 48: Audio
Speaker
  Creates arbitrary sound
Buzzer
  Creates a single or relatively narrow frequency of sound
  Often the oscillator is included

## Slide 49: Piezoelectric
Piezoelectric material flexes when a voltage is applied (conversely it generates a voltage when flexed)
Often used in low-profile buzzers

## Slide 50: Summary
Sensors
Noise
  Time Domain vs. Frequency Domain
  Filtering
Actuators
Next: Back to the ARM (SWI)