## Slide 1: 18-349: Introduction to Embedded Real-Time Systems
Anthony Rowe
Electrical and Computer Engineering
Carnegie Mellon University
Lecture 12: Mid-Term Review

## Slide 2: Administrivia
Lab 2 checkpoint Today
  Lab 2 due next Monday (Oct. 17th)
Mid-Term Exam on Wednesday
  Open book / note
  Will cover everything from lecture up to this point
  We will hit some highlights today

## Slide 3: Previous Lecture
Direct Memory Access (DMA)
Double Buffering
Processes
  Processes vs Threads
  Context Swap
  TCB

## Slide 4: Mid-Term Logistics
Takes place during normal lecture
Open book / open note
Bring a calculator!
No electronic communication (laptop and cellphone are not allowed)
Format
  Approximately 6 questions
  Mix of multiple choice and short answers
Comprehensive, but with a focus on what is not tested by the labs

## Slide 5: Overview
L1 – What is embedded?
L2 – ARM Architecture
L3 – ARM ASM
L4 – Memory Mapped I/O
L5 – Serial Buses
L6 – Timers and Interrupts
L7 – SWI
L8 – ADC and DAC
L9 – Transducers
L10 – ARM Optimization and Profiling
L11 – DMA and Processes

## Slide 6: Lecture 1: Intro to Embedded
What are embedded systems?
How is embedded different?
  Size, Power, Harsh Environments, Safety-Critical, Cost, Interfaces with Physical world
CPU
Cache
Memory
I/O
MMI
D/A
A/D
Microcontroller
Sensors
Actuator
Auxiliary Systems
(power, cooling)
Diagnostic
tools
External
Environment
Electro-mechanical
backup and safety
CPU
Cache
Memory
I/O
MMI
D/A
A/D
Microcontroller
Sensors
Actuator
Auxiliary Systems
(power, cooling)
Diagnostic
tools
External
Environment
Electro-mechanical
backup and safety
CPU
Cache
Memory
I/O
MMI
D/A
A/D
Microcontroller
Sensors
Actuator
Auxiliary Systems
(power, cooling)
Diagnostic
tools
External
Environment
Electro-mechanical
backup and safety
Network
Network
Network
Distributed!

## Slide 7: Overview of Fundamentals
Instructions, machine code
Instruction cycle, fetch cycle
Basics of interrupts
The memory pyramid
Caches
Pipelining
Big endian vs. little endian
Memory areas of a program
Moore’s Law
RISC vs. CISC

## Slide 8: Lecture 2: ARM Architecture
CISC vs RISC
Register Mapping / Modes
  Modes
  Register Banking
Exception vs Interrupt
  Why do we have them?

## Slide 9: Register Set
1
2
3
4
5
6
7
8
9
10
11
12
13
19
20
14
15
16
17
18
21
22
23
24
25
26
27
28
29
30
31
32
33
34
35
36
37
Notes: 6 different R13 registers

## Slide 10: Lecture 3: ARM ASM
Pipelining
  What is it?
  Why do we do it?
ASM Instructions
  Bring the ASM cheat sheet!
  Barrel Shifter
  Conditional Instructions
  Addressing Modes
  Load/Store Multiple

## Slide 11: Traditional ARM Pipeline
ARM traditionally employed a 3-stage pipeline with the following stages
  Fetch: instruction fetched from memory
  Decode: instruction is decoded
  Execute: instruction is executed
When processor is executing simple data processing instructions the pipeline enables one instruction to be completed every clock cycle
fetch decode execute
time
3
2
1
fetch decode execute
fetch decode execute

## Slide 12: The ARM Barrel Shifter
Data processing instructions are processed within the ALU
ARM can shift the 32-bit binary pattern in one of the source registers left or right by a specific number of positions before the value enters the ALU
Can achieve fast multiplies or division by a power of 2
Data-processing instructions that do not use the barrel shifter
  MUL (multiply)
  CLZ (count leading zeros)
  QADD (signed saturated 32-bit add)
Rn
Rm
Rd
Result N
Pre-processing
No pre-processing
Arithmetic and Logic
Unit (ALU)

## Slide 13: Value of Conditional
This improves code density and performance by reducing the number of forward branch instructions
  if (x != 0) CMP r3,#0 a = b+c; BEQ skip else ADD r0,r1,r2
  a = b–c; B afterskip
  skip
  SUB r0, r1, r2
  afterskip
CMP r3,#0 ADDNE r0,r1,r2
SUBEQ r0,r1,r2

## Slide 14: Addressing Modes
Preindex
  Same as preindex with writeback, but does not update the base register
  Example: LDR r0, [r1, #4]
Preindex with writeback
  Calculates address from a base register plus address offset
  Updates the address in the base register with the new address
  The updated base register value is the address used to access memory
  Example: LDR r0, [r1, #4]!
Postindex
  Only updates the base register after the address is used
  Example: LDR r0, [r1], #4

## Slide 15: Multiple-Register Transfer
Load-store-multiple instructions can transfer multiple registers between memory and the processor in a single instruction
Advantages
  More efficient than single-register transfers for moving blocks of data around memory
  More efficient for saving and restoring context and stacks
Disadvantages
  ARM does not interrupt instructions when executing a load-store multiple instructions can increase interrupt latency
Compilers can limit interrupt latency by providing a switch to control the max number of registers that can be transferred on a load-store-multiple
      LDM<cond><addrMode> Rn{!}, <registerList>{^}
      STM<cond><addrMode> Rn{!}, <registerList>{^}
Notes: {^} – denotes user registers from supervisor mode
{!} – write back (update Rn address when done)

## Slide 16: Lecture 4:
Memory Mapped I/O
  Why?
  How is it used?
Volatile
  Why?
  When should it be used?

## Slide 17: Thoughts on volatile
What does the keyword volatile accomplish?
  Tells the compiler not to perform certain optimizations
  Tells the compiler not to use the cached version of the variable
  Indicates that that variable can change asynchronously
Some compilers allow you to declare everything as volatile
  Don’t! It’s a substitute for good thinking
  Can lead to less efficient code
Don’t blame the optimizer and don’t turn it off
If you are given a piece of code whose behavior is unpredictable
  Look for declarations of volatile variables
  Look for where you should declare a variable as volatile

## Slide 18: Lecture 5: Serial Buses
Serial vs Parallel
  Why choose one over the other?
Asynchronous vs Synchronous Communication
Know your buses!
  UART, SPI, I2C
  What are the trade-offs?
Serial Bus Concepts
  Framing (start/stop bits)
  Baudrate
  Error checking (parity)

## Slide 19: Serial vs. Parallel
MCU 1
MCU 2
TX
RX
MCU 1
MCU 2
signal
Data[0:7]
Serial
Parallel

## Slide 20: Sync vs. Async
Synchronous communications
  Requires common clock (SPI)
  Whoever controls the clock controls communication speed
Asynchronous communications
  Has no clock (UART)
  Speed must be agreed upon beforehand (the baud-rate configuration accomplishes that)

## Slide 21: UART
Source: Dallas Semiconductors
Application note 83
Notes: 21
With 1 or 2 stop bits the line output is held at the mark level for 1 or 2 times a bit duration.
With 1.5 stop bits imply that the line output is held at the mark level for 1.5 times a single bit duration, useful in detecting certain synchronization errors because if there is an immediate character to be TX/RX next it’s start bit would cause a change in the voltage level in the middle of a bit signifying the definite presence of a stop bit
Width of a bit is determined by baud rate. 9600 baud, 1 bit=1/9600=0.104 mS. So, start bit would be held for 0.104ms

## Slide 22: SPI Communication

## Slide 23: I2C
First byte of transfer contains the slave address and the data direction
  Address is 7 bits long, followed by the direction bit
  Like all data bytes, address is transferred with the most significant bit first
7-bit address space allows for 128 unique I2C device addresses
  16 addresses are reserved for special purposes
  Leaves only 112 addresses with this 7-bit address scheme
New 10-bit address scheme has been introduced
“General call” broadcast – to address every device on the bus
What is the maximum number of devices in I2C limited by?
Notes: The maximum number of nodes is obviously limited by the address space, and also by the total bus capacitance of 400 pF.

## Slide 24: Lecture 6: Timers and Interrupts
What is a timer?
Polling vs. Interrupt Driven
  What is the difference?
  When using Polling?
  When use Interrupts?
Implications around Interrupts
  FIQ vs. IRQ
  Nest vs. non-nested

## Slide 25: What is a Timer?
A device that uses a high­speed clock input to provide a series of time or count-related events
÷
000000
0x1206
I/O Control
Clock Divider
Counter Register
Reload on Zero
Countdown Register
Interrupt to Processor
System Clock

## Slide 26: Polling vs. Interrupt­Driven I/O
Polling requires code to loop until device is ready
  Consumes lots of CPU cycles
  Can provide quick response (guaranteed delay)
Interrupts don't require code to loop until the device is ready
  Device interrupts processor when it needs attention
  Code can go off and do other things
  Interrupts can happen at any time
    Requires careful coding to make sure other programs (or your own) don't get messed up
What do you think real-time embedded systems use?

## Slide 27: Lecture 7: Software Interrupts
System Calls
  What are they?
  Why are they useful?
  How are the implemented?
SWI overview for ARM

## Slide 28: System Calls
Application Program
Standard C Library
Operating System
Hardware Device
Driver
Hardware
Device
swi
fread()

## Slide 29: Vectoring to an SWI
LDR pc, [pc, 0x100]
LDR pc, [pc, 0x100]
LDR pc, [pc, 0x100]
LDR pc, [pc, 0x100]
LDR pc, [pc, 0x100]
LDR pc, [pc, 0x100]
LDR pc, [pc, 0x100]
LDR pc, [pc, 0x100]
Vector Table
starting at 0x00 in memory
0x00
0x04
0x08
0x0c
0x10
0x14
0x18
0x1c
SWI Handler
(S_Handler)
2
&A_Handler
&U_Handler
&S_Handler
&P_Handler
...
“Jump” Table
0x108
0x10c
0x110
0x114
...
ADD r0,r0,r1
SWI 0x10
SUB r2,r2,r0
USER Program
softvec
MOVS pc, lr
3

## Slide 30: Lecture 8: ADC and DAC
Understand converting between physical phenomena -> Engineering units in a CPU
ADC and DAC
  Concepts
  What is anti-aliasing?
Software
Sensor
ADC
Physical
Phenomena
Voltage or
Current
ADC Counts
Engineering Units

## Slide 31: Lecture 9: Transducers
Sensors
  Types and properties
Actuators
  Types and properties
Sampling Rate and Resolution
  Not much if any digital filtering since it has not been covered in lab yet

## Slide 32: Lecture 10: Optimization
System Profiling
  What can we measure and how?
Optimization Techniques
  Understand what smart compilers do under the hood
  Trade-offs
    Performance vs. Size
    Negative Instruction-cache effect

## Slide 33: Optimization Overview
Code Optimization Techniques
  Processor independent compiler optimizations
    Common sub-expression elimination
    Dead-code elimination
    Induction variables
    In-lining of functions
    Loop unrolling
ARM specific optimization
    Count-down loops
    Register spilling
    Efficient use of global variables
Space Optimization

## Slide 34: Lecture 11:
DMA
  Really important natural extension of MMIO
Double Buffering
  Downplayed on exam since it hasn’t been covered in lab yet
Process vs Thread
Process State

## Slide 35: Direct Memory Access (DMA)
What if we make the device a little smarter??
  Make the device capable of moving data to/from memory itself
  Advantage: it would no longer need the processor to move the data
  Disadvantage: more complicated
Processor
device
On-chip
cache
Memory
buffer
program
Bus
... while the processor executes instructions for another process
DMA reads/writes memory

## Slide 36: Process vs. Task vs. Thread
The terms, process and task, are often used interchangeably
Threads, sometimes called lightweight processes, consist of
  Program counter
  Register set
  Stack space
A single process (task) can have multiple threads
These multiple threads share the text and data segments (physical memory), file descriptors and process priority
Each thread has its own private register set (including PC) and stack

## Slide 37: Process State
Waiting
for
Event
Dormant
Ready
Running
Interrupted
task
deleted
interrupted
task create
task deleted
context switch
event
occurred
wait for
event
task delete
context switch

## Slide 38: How to study
Do old practice exams
  Head to the review session for a walkthrough and solutions
Organize and Read through slides
Ask lots of questions!

## Slide 39: Good Luck!