## Slide 1: Introduction to Embedded & Real-Time Systems
Sathish Gopalakrishnan
Electrical and Computer Engineering
The University of British Columbia
sathish@ece.ubc.ca
Real-Time Scheduling 1

## Slide 2: Metrics in Real-Time Systems – I
End-to-end latency:
  E.g. worst-case, average-case, variance, distribution
  Can involve multiple hops (across nodes, links, switches and routers)
  Behavior in the presence or absence of failures
Jitter
  Variability in metrics (e.g., variability in throughput)
Throughput
  How many requests can be processed in unit time?
  How many messages can be transmitted in unit time?
Robustness
  How many faults can be tolerated before system failures?
  What functionality gets compromised?

## Slide 3: Metrics in Real-Time Systems – II
Safety & Certification
  Is the system “safe”?
  Can the system get into an ‘unsafe’ state? Has it been ‘certified’?
Modes and reconfiguration
  What happens when the system mission changes?
  What happens under mode changes?
    What are examples of mode changes?
  What happens when individual elements fail?
  Can the system reconfigure itself dynamically?
  How does the system behave after re-configuration?
Security
  Can the system’s integrity be compromised?
  Can violations be detected?
  Renewed interest in this area with appliances being connected to the Internet

## Slide 4: Scheduling
Scheduler = resource allocator that affects the timing of real-time services
Offline scheduler = does allocation at design time
Online scheduler = does allocation at run-time
Schedulers need to know dependencies and worst-case behavior
Worst-case execution time (WCET) is often required to be known in real-time systems
How do you determine worst-case behavior?

## Slide 5: Classification of Scheduling Algorithms
All scheduling algorithms
static scheduling
(or offline, or clock driven)
dynamic scheduling
(or online, or priority driven)
static-priority
scheduling
dynamic-priority
scheduling

## Slide 6: Scheduling Algorithms (No Priority)
Non-priority-based
  All tasks are created equal
  There is no way to indicate which tasks are more “important” (more critical) than others
First-In-First-Out (FIFO) or First-Come-First-Served (FCFS)
  Ready tasks are inserted into a list
  Tasks are dispatched from the list in their order of entry in the list
  No preemption, i.e., a task runs to completion before the next task runs
  No consideration of task priorities
Round-Robin Preemptive
  Ready tasks are dispatched in turn
  Each task given its fair share of fixed execution time
  Preemption of running task at the end of the fixed interval
  No consideration of task priorities

## Slide 7: Scheduling Algorithms (Fixed-Priority)
Fixed-priority based
  All tasks are not created equal
  Some tasks have more importance (higher priority) than others
  Once a task’s priority is assigned, it cannot change during run-time
Rate Monotonic Analysis (RMA)
  Shorter the period, the higher the priority of the task
  Assigns fixed priorities in reverse order of period length
  Tasks requiring frequent attention have higher priority and get scheduled earlier
Least Compute Time (LCT)
  Shorter the computation time, the higher the priority of the task
  Assigns fixed priorities in reverse order of computation length
  Tasks finishing quickly have higher priority and get scheduled earlier

## Slide 8: Scheduling Algorithms (Dynamic-Priority)
Dynamic-priority based
  All tasks are not created equal
  Some tasks have more importance (higher priority) than others
  Task’s priority (and thus, the schedule) may change during execution
Shortest Completion Time (SCT)
  Ready task with the smallest remaining compute time gets scheduled first
Earliest Deadline First (EDF)
  Ready task with the earliest future deadline gets scheduled first
Least Slack Time (LST)
  Ready task with the smallest amount of free/slack time within the cycle gets scheduled first

## Slide 9: Example of Priority Assignment
0
25
VIP:
0
10
20
30
IP:
Semantics-Based Priority Assignment
misses deadline
0
10
20
30
IP:
0
25
VIP:
Policy-Based Priority Assignment
τi = { Ci , Ti }
VIP = { 10, 25 }
IP = {1,10}
Notes: 5
This example provides some motivation for using the rate monotonic scheduling algorithm. In the example we have 2 tasks, named IP and VIP, with the following descriptions:
Task IP: CIP = 1; TIP = 10; UIP = 0.10
Task VIP: CVIP = 11; TVIP = 25; UVIP = 0.44
Total utilization: 54%
If we assign higher priority to task VIP, then task IP will miss its deadline, even though the total utilization is only 54%. But if priorities are assigned according to the rate monotonic algorithm, then both tasks will meet their deadlines. Notice that, as VIP’s period increases, total utilization decreases to 10%, since UVIP approaches zero for large TVIP; yet deadlines are still missed

## Slide 10: Why Are Deadlines Missed?
For a given task, consider
  Preemption: time waiting for higher priority tasks
  Execution: time to do its own work
  Blocking: time delayed by lower priority tasks
The task is schedulable if the sum of its preemption, execution, and blocking is less than its deadline.
Focus: identify the biggest hits among the three and reduce, as needed, for schedulability
Notes: 9
Note:
For a task to meet its deadline, it must accommodate
Preemption from higher-priority tasks,
Its own execution time, and
Delays caused by lower-priority tasks (known as priority inversion or blocking).
Remember that higher-priority tasks, from a rate monotonic perspective, are those with higher rates (or shorter periods). These can occur more than once in a task’s period. A task’s execution occurs once during its period. And blocking can occur at most once during the task’s period; blocking comes from lower-priority tasks, those that have slower rates (or longer periods).
Preemption and execution are unavoidable. If these exceed capacity, one is faced with a classical throughput problem and the only remedy is to reduce the workload (which means changing the system requirements) or to increase the capacity by using a faster computer. Experience has shown that priority inversion (blocking), delay from lower-priority tasks, is a major source of missed deadlines. So we focus on identifying sources of priority inversion and try to reduce their blocking effects to enhance schedulability.

## Slide 11: Drift and Jitter
Drift can be eliminated completely but one can only
hope to minimize jitter in general

## Slide 12: Sources of Drift and Jitter
What can cause drift?
What can cause jitter?
How would you prevent drift?
How would you prevent jitter?
If I gave you a piece of code and asked you to spot all of the places where jitter and drift could occur, how you would go about it?
Notes: think of paging, multi-tasking and preemption

## Slide 13: Real-Time Standards
Real-Time Operating System standards
  IEEE 1003.1b POSIX Real-Time Extensions
  OSEK (automotive real-time OS standard)
Real-Time (and Concurrent) Programming Languages
  Real-Time Specification for Java
  Ada 83 and Ada 95
Real-Time Middleware
  Real-Time CORBA
Networks/buses
  CANbus (Controller Area Network bus)
  TTA: Time-Triggered Architecture (www.tttech.com)
  FlexRay (www.flexray.org)

## Slide 14: Plan for Lecture(s)
Present basic theory for periodic task sets
Extend basic theory to include
  context switch overhead
  preperiod deadlines
  interrupts
Consider task interactions:
  priority inversion
  synchronization protocols (time allowing)
Extend theory to aperiodic tasks:
  sporadic servers (time allowing)
Notes: 25
The approach that we will take with this tutorial is to start with very simple concepts and gradually build onto this foundation with more practical, real-world considerations.
We will first introduce the mechanics of RMA, applying the basic theory for independent, periodic tasks.
We will then extend the basic theory to include practical issues, such as context switch overhead, interrupts, and non-rate-monotonic priority assignments.
We will present a case study that incorporates the strategies covered and demonstrates the benefits of using RMA.
There will be exercises associated with some sections to practice the concepts discussed in those modules.
Next, as time allows, we will consider task interaction and aperiodic events, incorporating these issues into the analysis

## Slide 15: A Sample Problem
Periodics Resources Aperiodics
t
1
t
2
t
3
20 msec
40 msec
100 msec
100 msec
150 msec
350 msec
20 msec
Data Server
2 msec
10 msec
Comm Server
10 msec
5 msec
Emergency
50 msec
Deadline 6 msec
after arrival
2 msec
Routine
40 msec
Desired response
20 msec average
t2’s deadline is 20 msec before the end of each period
Notes: 26
We will use this sample problem throughout the tutorial as a common thread, starting with the periodic tasks, then gradually adding the other components in the task set. This sample task set is simple and yet embodies many different types of real-time requirements. The task set is completely analyzable using the methods outlined in this tutorial.
Task set characteristics:
Periodic task t1: execution time = 20 msec; period = 100 msec; deadline is at the end of each period.
In addition, t3 may block t1 for 10 msec by using a shared communication server, and task t2 may block t1 for 20 msec by using a shared data object.
Periodic task t2: execution time = 40 msec; period = 150 msec; deadline is 20 msec before the end of each period.
Periodic task t3: execution time = 100 msec; period = 350 msec; deadline is at the end of each period.
Emergency event handling task: execution time = 5 msec; worst-case interarrival time = 50 msec; deadline is 6 msec after arrival.
Routine event handling task: average execution time = 2 msec; average interarrival time = 40 msec; 4 msec average response time is needed.

## Slide 16: Rate Monotonic Analysis
Introduction
Periodic tasks
Extending basic theory
Synchronization and priority inversion
Aperiodic servers
Notes: 1

## Slide 17: A Sample Problem - Periodics
Periodics Resources Aperiodics
t
1
t
2
t
3
20 msec
40 msec
100 msec
100 msec
150 msec
350 msec
20 msec
Data Server
2 msec
10 msec
Comm Server
10 msec
5 msec
Emergency
50 msec
Deadline 6 msec
after arrival
2 msec
Routine
40 msec
Desired response
20 msec average
t2’s deadline is 20 msec before the end of each period

## Slide 18: Rate Monotonic Scheduling
Optimal Static Priority Scheduling
A task with a shorter period has a higher deadline
  Shorter Period -> Higher priority
Assumption: Period is equal to Deadline
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
1
2
{1,4}
{2,5}
{ C,T }
3
{2,10}

## Slide 19: Rate Monotonic Scheduling
Optimal Static Priority Scheduling
A task with a shorter period has a higher deadline
  Shorter Period -> Higher priority
Assumption: Period is equal to Deadline
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
1
2
{1,4}
{2,5}
{ C,T }
3
{2,10}

## Slide 20: Rate Monotonic Scheduling
Optimal Static Priority Scheduling
A task with a shorter period has a higher deadline
  Shorter Period -> Higher priority
Assumption: Period is equal to Deadline
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
1
2
{1,4}
{2,5}
{ C,T }
3
{2,10}

## Slide 21: Rate Monotonic Scheduling
Optimal Static Priority Scheduling
A task with a shorter period has a higher deadline
  Shorter Period -> Higher priority
Assumption: Period is equal to Deadline
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
1
2
{1,4}
{2,5}
{ C,T }
3
{2,10}

## Slide 22: Rate Monotonic Scheduling
Optimal Static Priority Scheduling
A task with a shorter period has a higher deadline
  Shorter Period -> Higher priority
Assumption: Period is equal to Deadline
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
1
2
{1,4}
{2,5}
{ C,T }
3
{2,10}

## Slide 23: Rate Monotonic Scheduling
What does “Optimal” mean?
  If any possible fixed (static) priority combination could work, then RMS will work
Rate Monotonic Analysis (RMA)
  The proof that an RMS scheme is schedulable
  Liu and Leyland ( “Scheduling Algorithms for Multiprogramming in a Hard Real-Time Environment”, JACM, 1973)

## Slide 24: Concepts and Definitions - Periodics
Periodic task
  initiated at fixed intervals
  must finish before start of next cycle
Task’s CPU utilization:
  Ci = worst-case compute time (execution time) for task ti
  Ti = period of task ti
CPU utilization for a set of tasks
U = U1 + U2 +...+ Un
Ui =
Ci
Ti
Notes: 3
A periodic task becomes ready to execute at fixed intervals. The time between task initiations is called the period of the task. When we say a periodic task meets its deadline, we mean that it finishes its execution before the start of the next period (i.e. the end of the current period). This is not always the most appropriate definition for a periodic task’s deadline. For example, a requirement to minimize jitter means that a task must perform some action at a specific time, not simply before a specific time. Jitter can be minimized by several design approaches. One approach is to trigger a very high priority task by an accurate clock to meet a jitter requirement.
Ci and Ti represent the execution time and period respectively for task ti. A task’s utilization of the CPU is Ci/Ti. Total CPU utilization is the sum of the utilizations of all the tasks

## Slide 25: Schedulability: UB Test
Utilization bound (UB) test: a set of n independent periodic tasks scheduled by the rate monotonic algorithm will always meet its deadlines, for all task phasings, if
U(1) = 1.0 U(4) = 0.756 U(7) = 0.728
U(2) = 0.828 U(5) = 0.743 U(8) = 0.724
U(3) = 0.779 U(6) = 0.734 U(9) = 0.720
For harmonic task sets, the utilization bound is U(n)=1.00 for all n.
--- + .... + --- < U(n) = n(2 - 1)
C1 Cn 1/ n
T1 Tn
Notes: 6
We say a set of tasks is schedulable if the task set is guaranteed to meet all its deadlines. The utilization bound test says that a task set is schedulable if its total utilization is less than a certain bound, called the Liu & Leyland bound. The utilization bound test provides the basic formula underlying the theory. More complex formulas provide better bounds. This test is the application of a theorem, which was proved by Liu and Leyland in “Scheduling Algorithms for Multiprogramming in a Hard Real-Time Environment”, JACM, 1973.
The utilization bound test assumes that:
1. The processor always executes the highest priority task.
2. Task priorities are assigned according to rate monotonic policy.
3. Tasks do not synchronize with each other.
4. Each task’s deadline is at the end of its period.
5. Tasks do not suspend themselves in the middle of computations.
The test takes into account the preemption time and execution time for each task under a worst-case combination of periods and execution times. As the number of tasks goes to infinity, the bound approaches ln(2) = 0.693; in other words, any number of independent periodic tasks will meet their deadlines if the total system utilization is under 69%
For a harmonic task set (in which the period of each task is a multiple of all higher-frequency tasks), the utilization bound is 1.0 for all task sets.

## Slide 26: RMS Utilization Bound
Real-time system is schedulable under RM if
    Limit of n (21/n-1) as n->inf = 0.69

## Slide 27: Sample Problem: Applying UB Test
Total utilization is .200 + .267 + .286 = .753 < U(3) = .779
The periodic tasks in the sample problem are schedulable according to the UB test
C T U
Task t1: 20 100 0.200
Task t2: 40 150 0.267
Task t3: 100 350 0.286
Notes: 7
Since we are interested in worst-case behavior, tasks utilizations are always rounded up. For example, U2 = 40/150 = .2666... becomes .267 and U3 = 100/350 = .2857143... becomes .286.
In this example, since the total utilization is under the bound for three tasks, all tasks are guaranteed to meet their deadlines, even under worst-case conditions. An additional 24.7% CPU capacity is available for lower-priority tasks that have no deadline.
Remember that there are several assumptions associated with the utilization bound test:
Zero context switch overhead.
Deadlines are at end of period.
No interrupts are used.
Priorities are assigned in rate monotonic order.
Tasks do not interact with one another.
Tasks do not suspend themselves.

## Slide 28: Timeline for Sample Problem
0
100
200
300
400
Scheduling Points
t
2
t
3
t
1
Notes: 8
This is the timeline for the periodic tasks of the sample problem (shown on the previous page), in which tasks are lined up in worst-case phasing (i.e. all task are ready to execute at time t=0).
Timelines show one possible execution schedule and provide a graphical view of schedule analysis. We will draw timelines according to the following conventions:
Tasks are arranged and numbered in rate monotonic order, highest frequency at the top.
We assume Liu and Leyland “worst-case” phasing, where all tasks start at time t=0.
Execution time for t1 is plotted on its line.
Execution time for t2 is then plotted on its line, accommodating preemption from t1’s execution; then this process is repeated for remaining tasks.
If any task is preempted, its execution time block is divided with a hole in the middle representing the preemption (e.g. t3)

## Slide 29: Exercise: Applying the UB Test
a. What is the total utilization?
b. Is the task set schedulable?
c. Draw the timeline.
d. What is the total utilization if C3 = 2 ?
Given:
C T U
Task t1: 1 4
Task t2: 2 6
Task t3: 1 10
Notes: 7
Since we are interested in worst-case behavior, tasks utilizations are always rounded up. For example, U2 = 40/150 = .2666... becomes .267 and U3 = 100/350 = .2857143... becomes .286.
In this example, since the total utilization is under the bound for three tasks, all tasks are guaranteed to meet their deadlines, even under worst-case conditions. An additional 24.7% CPU capacity is available for lower-priority tasks that have no deadline.
Remember that there are several assumptions associated with the utilization bound test:
Zero context switch overhead.
Deadlines are at end of period.
No interrupts are used.
Priorities are assigned in rate monotonic order.
Tasks do not interact with one another.
Tasks do not suspend themselves.

## Slide 30: Solution: Applying the UB Test
a. What is the total utilization? .25 + .34 + .10 = .69
b. Is the task set schedulable? Yes: .69 < U(3) = .779
c. Draw the timeline.
d. What is the total utilization if C3 = 2 ?
.25 + .34 + .20 = .79 > U(3) = .779
0
5
10
15
20
Task t1
Task t3
Task t2
Notes: 8
This is the timeline for the periodic tasks of the sample problem (shown on the previous page), in which tasks are lined up in worst-case phasing (i.e. all task are ready to execute at time t=0).
Timelines show one possible execution schedule and provide a graphical view of schedule analysis. We will draw timelines according to the following conventions:
Tasks are arranged and numbered in rate monotonic order, highest frequency at the top.
We assume Liu and Leyland “worst-case” phasing, where all tasks start at time t=0.
Execution time for t1 is plotted on its line.
Execution time for t2 is then plotted on its line, accommodating preemption from t1’s execution; then this process is repeated for remaining tasks.
If any task is preempted, its execution time block is divided with a hole in the middle representing the preemption (e.g. t3)

## Slide 31: Toward a More Precise Test
UB test has three possible outcomes:
0 < U < U(n)  Success
U(n) < U < 1.00  Inconclusive
1.00 < U  Overload
UB test is conservative.
A more precise test can be applied.
Notes: 9
The results of applying the UB test can be:
0<U<u(n) success, task set is schedulable
U9n)<U<1.0 inconclusive, task set may or may not be schedulable
1.0 < U overload, task set exceeds capacity
When the UB test is inconclusive, a more precise test can be applied.
The previous schedulability test (utilization bound test) is very conservative. Schedulable system utilization can often exceed 90%. In fact, for tasks with harmonic periods, where each period is evenly divisible into all longer periods (e.g. 100 ms, 200 ms, 800 ms, 1600 ms), the utilization bound is 100%.

## Slide 32: Schedulability: RT Test
Theorem: The worst-case phasing of a task occurs when it arrives simultaneously with all its higher priority tasks.
Theorem: for a set of independent, periodic tasks, if each task meets its first deadline, with worst-case task phasing, the deadline will always be met.
Response time (RT) or Completion Time test: let an = response time of task i. an of task i may be computed by the following iterative formula:
Test terminates when an+1 = an.
Task i is schedulable if its response time is before its deadline: an < Ti
The above must be repeated for every task i from scratch
a
n+1
C
i
a
n
T
j
C
j
j
1
=
i
1
-
å
+
where a
0
C
j
j
1
=
i
å
=
=
This test must be repeated for every task ti if required
  i.e. the value of i will change depending upon the task you are looking at
Stop test once current iteration yields a value of an+1 beyond the deadline (else, you may never terminate).
The ‘square bracketish’ thingies represent the ‘ceiling’ function, NOT brackets
Notes: 10
This remarkable theorem was proved by Liu and Leyland and assumes:
Tasks are scheduled according to the rate monotonic algorithm.
Tasks are independent and do not interact.
Tasks do not suspend during execution.
The iterative formula for task response time was introduced in Joseph and Pandya, “Finding Response Times in a Real-Time System,” BCS Computing Journal, October 1986 (vol 29 no 5) pp 390-395.
The iterative formula is an application of fixed point iteration. Since the successive iterates are non-decreasing and approach the response time from below, the iterative formula is known to converge if there is a solution.
There is an alternative approach that we call the scheduling point version of the response time test (see slide 29). The mathematical characterization of this scheduling point version is presented in The Rate Monotonic Scheduling Algorithm -- Exact Characterization and Average Case Behavior, by Lehoczky, Sha, and Ding, Technical Report, Department of Statistics, Carnegie Mellon University, 1987. Also presented in this paper is the fact that for randomly generated task sets, the actual utilization bound is 88% rather than the worst-case bound of 69% presented in the UB test.

## Slide 33: Example: Applying RT Test -1
Taking the sample problem, we increase the compute time of t1 from 20 to 40; is the task set still schedulable?
Utilization of first two tasks: 0.667 < U(2) = 0.828
  first two tasks are schedulable by UB test
Utilization of all three tasks: 0.953 > U(3) = 0.779
  UB test is inconclusive
  need to apply RT test
C T U
Task t1: 20 100 0.200
Task t2: 40 150 0.267
Task t3: 100 350 0.286
0.4
40
Notes: 11
The following data is the same as the sample problem. However, we have changed C1 from 20 to 40 to illustrate the use of the RT test.
Task t1: C1 = 40; T1 = 100; U1 = 0.4
Task t2: C2 = 40; T2 = 150; U2 = 0.267
Task t3: C3 = 100; T3 = 350; U3 = 0.286
Utilization of first two tasks: .4 + .267 = .667 < U(2) = .828
Total utilization: .4 + .267 + .286 = .953 > U(3) = .779
When we change C1 from 20 to 40, CPU utilization changes. Since the utilization of the first two tasks is under the utilization bound of the UB test, these tasks will always meet their deadlines. When the third task is considered, the total utilization is above the utilization bound (Liu & Leyland), so we must look further to see if the third task can nonetheless meet its deadline.
We will now apply the response time test to task t3

## Slide 34: Example: Applying RT Test -2
Use RT test to determine if t3 meets its first deadline: i = 3
100
180
100
40
(
)
180
150
40
(
)
+
+
100
80
80
+
+
260
=
=
=
a
1
C
i
a
0
T
j
C
j
j
1
=
i
1
-
å
+
C
3
a
0
T
j
C
j
j
1
=
2
å
+
=
=
3
a
0
C
j
j
1
=
å
C
1
C
2
C
3
+
+
40
40
100
+
+
180
=
=
=
=
Notes: 12
To apply the RT test, we do two steps
Use the iterative formula to compute the first response time W3 of t3.
Compare W3 to the first deadline for t3, namely T3.
If W3 < T3, then t3 is schedulable according to the RT test.
We start with an initial guess W3 = 0. This is labeled as the “zero-ith” iteration W3(0) = 0. To compute the first iteration, W3(1), we use the iteration formula with n = 0.
Substitute 0 for W3(0). All the terms in the summation drop out, so the first iteration is
W3(1) = C3 = 100.
Next we apply the formula with n=1 and n=2, and compute, respectively, W3(2) and W3(3). Since each successive iteration is different, the computation has not yet converged and we must continue.

## Slide 35: Example: Applying the RT Test -3
Task t3 is schedulable using RT test
a
3
300
=
T
<
350
=
a
2
C
3
a
1
T
j
C
j
j
1
=
2
å
+
=
100
260
100
(40)
260
150
(40)
+
+
=
= 300
a
3
a
2
300
Done!
=
=
a
3
C
3
a
2
T
j
C
j
j
1
=
2
å
+
=
100
300
100
(40)
300
150
(40)
+
+
=
= 300
Notes: 13
We continue by applying the iteration formula for n=3 and n=4.
Finally, the computed value for W3(5) is the same as W3(4).
W3(5) = W3(4) = 300.
The iteration has converged, and the first response time for t3 is
W3 = 300.
This must be compared to the first deadline for t3.
We have W3 < T3 since 300 < 350.
So t3 is schedulable using the response time test.

## Slide 36: Timeline for Example
t
2
t
3
0
100
200
300
t
1
t
3
completes its work at t = 300
Notes: 14
This slide illustrates an alternate version of the response time test based on scheduling points. Again, the test is being applied only to t3.
A scheduling point is a point in time when new work arrives; the beginning of a new period for some task in the task set. This version of the CT test checks to see if there exists a scheduling point (at or before the deadline of t3) at which all work initiated up to that point has been completed. Since the workload includes the compute time of t3 as well as all higher-priority tasks, if the work is completed, then t3 has met its deadline.
In this graphical representation of task execution under worst-case phasing, we can see that, when all tasks are ready to execute at t=0, task t3 cannot begin execution until t=80. As t3 tries to complete its work it gets preempted at the next scheduling point at t=100, where t1 introduces more work. Each time t3 resumes its work it is preempted before completion, until t=300. In this example, task t3 completes all its work at exactly the fourth scheduling point. It completes all its work before its first deadline at t=350, and is therefore schedulable.
The reason for introducing two ways to find the response time is that the iteration formula is easier to program, while the scheduling points are easier to visualize

## Slide 37: Exercise: Applying RT Test
Task t1: C1 = 1 T1 = 4
Task t2: C2 = 2 T2 = 6
Task t3: C3 = 2 T3 = 10
a) Apply the UB test
b) Draw timeline
c) Apply RT test
Notes: 7
Since we are interested in worst-case behavior, tasks utilizations are always rounded up. For example, U2 = 40/150 = .2666... becomes .267 and U3 = 100/350 = .2857143... becomes .286.
In this example, since the total utilization is under the bound for three tasks, all tasks are guaranteed to meet their deadlines, even under worst-case conditions. An additional 24.7% CPU capacity is available for lower-priority tasks that have no deadline.
Remember that there are several assumptions associated with the utilization bound test:
Zero context switch overhead.
Deadlines are at end of period.
No interrupts are used.
Priorities are assigned in rate monotonic order.
Tasks do not interact with one another.
Tasks do not suspend themselves.

## Slide 38: Solution: Applying RT Test
a) UB test
  t1 and t2 OK -- no change from previous exercise
  .25 + .34 + .20 = .79 > .779 ==> Test inconclusive for t3
b) RT test and timeline
0
5
10
15
20
Task t1
Task t2
Task t3
All work completed at t = 6
Notes: 8
This is the timeline for the periodic tasks of the sample problem (shown on the previous page), in which tasks are lined up in worst-case phasing (i.e. all task are ready to execute at time t=0).
Timelines show one possible execution schedule and provide a graphical view of schedule analysis. We will draw timelines according to the following conventions:
Tasks are arranged and numbered in rate monotonic order, highest frequency at the top.
We assume Liu and Leyland “worst-case” phasing, where all tasks start at time t=0.
Execution time for t1 is plotted on its line.
Execution time for t2 is then plotted on its line, accommodating preemption from t1’s execution; then this process is repeated for remaining tasks.
If any task is preempted, its execution time block is divided with a hole in the middle representing the preemption (e.g. t3)

## Slide 39: Solution: Applying RT Test (cont.)
c) RT test
3
a
0
C
j
j
1
=
å
C
1
C
2
C
3
+
+
1
2
2
+
+
5
=
=
=
=
a
1
C
3
a
0
T
j
C
j
j
1
=
2
å
+
=
=
2
5
4
1
+
5
6
2
+
=
2 + 2 + 2 = 6
a
2
C
3
a
1
T
j
C
j
j
1
=
2
å
+
=
=
2
6
4
1
+
6
6
2
+
=
2 + 2 + 2 = 6
Done
Notes: 8
This is the timeline for the periodic tasks of the sample problem (shown on the previous page), in which tasks are lined up in worst-case phasing (i.e. all task are ready to execute at time t=0).
Timelines show one possible execution schedule and provide a graphical view of schedule analysis. We will draw timelines according to the following conventions:
Tasks are arranged and numbered in rate monotonic order, highest frequency at the top.
We assume Liu and Leyland “worst-case” phasing, where all tasks start at time t=0.
Execution time for t1 is plotted on its line.
Execution time for t2 is then plotted on its line, accommodating preemption from t1’s execution; then this process is repeated for remaining tasks.
If any task is preempted, its execution time block is divided with a hole in the middle representing the preemption (e.g. t3)

## Slide 40: Summary
UB test is simple but conservative.
RT test is more exact but also more complicated.
To this point, UB and RT tests share the same limitations:
  all tasks run on a single processor
  all tasks are periodic and noninteracting
  deadlines are always at the end of the period
  there are no interrupts
  Rate-monotonic priorities are assigned
  there is zero context switch overhead
  tasks do not suspend themselves
Notes: 15
Although the UB test is conservative, it is useful in providing insight into timing issues. The BSY-1 case study will illustrate this.
Step-by-step algorithms are available in the A Practitioner's Handbook for Real-Time Analysis (published by Kluwer).
Up to this point in the tutorial, the schedulability tests have the following limiting assumptions:
All tasks run on a single processor.
All tasks are periodic and noninteracting.
Deadlines of all tasks are at the end of the period.
No interrupts are used.
Rate monotonic priorities are assigned.
There is no context switch overhead.
Tasks do not suspend themselves.
We will relax some of these assumptions in the next several sections.

## Slide 41: Rate Monotonic Analysis
Introduction
Periodic tasks
Extending the basic theory
Synchronization and Priority Inversion
Aperiodic servers

## Slide 42: A Sample Problem
t2’s deadline is 20 msec before the end of each period
Periodics Resources Aperiodics
t
1
t
2
t
3
20 msec
40 msec
100 msec
100 msec
150 msec
350 msec
20 msec
Data Server
2 msec
10 msec
Comm Server
10 msec
5 msec
Emergency
50 msec
Deadline 6 msec
after arrival
2 msec
Routine
40 msec
Desired response
20 msec average

## Slide 43: Extensions to Basic Theory
This section extends the schedulability tests to address
  nonzero task switching times
  preperiod deadlines
  interrupts and non-rate-monotonic priorities
Notes: To this point we have assumed that there was no context (or task) switching overhead, that all deadlines were at the end of the period, and that tasks were scheduled according to the rate monotonic algorithm. In particular, we have assumed perfect preemption for the priority-based scheduler and we have assumed that priorities are assigned rate monotonically. Lack of preemption has the effect of delaying (or blocking) higher-priority tasks until the lower-priority task finishes its nonpreemptive execution. This situation in which a higher-priority task is ready to run, yet is prevented from running by a lower-priority task, we call priority inversion. Another source of priority inversion (from the standpoint of rate monotonic theory) is when priorities are assigned to tasks in violation of the rate monotonic algorithm. In this situation, a longer-period task (with a higher scheduling priority) will delay the execution of a task with a higher rate monotonic priority

## Slide 44: Modeling Task Switching as Execution Time
time
S
S
S
S
S
C
1
C
2
C
2
t
3
t
2
t
1
40
0
100
200
C
1
C
2
C
2
C
1
C
1
T
1
T
2
2T
1
C
i
+ 2S
T
i
U
i =
Two scheduling actions per task
(start of period and end of period)
40
C
1
C
1
Notes: When a task preempts a lower-priority task, the execution state of the lower-priority task is saved and the execution state of the higher-priority task is established. When the higher- priority task completes its processing and relinquishes the CPU to a lower-priority task, its execution state is saved and the state of the lower-priority task is reestablished. The context switches for (1) preemption of the lower-priority process and (2) subsequent resumption of its execution account for the 2S added to the execution time of the preempting process.
Consider a given task, t3, which may be preempted by higher-priority tasks, t1 and t2. Worst case is that t3 will be preempted by t1 (and t2) every time t1 (or t2) is ready to run. Each preemption causes two context switches; one from t3 to run t1 and one from t1 back to resume t3. These two context switch times are charged to the higher-rate preempting task.

## Slide 45: Modeling Preperiod Deadlines
Suppose task t, with compute time C and period T, has a preperiod deadline D (i.e. D < T ).
Compare total utilization to modified bound:
where Di is the ratio (Di / Ti).
U(n, Di) =
n
2
D
i
(
)
1
n
¤
1
-
(
)
1
D
i
-
+
1
2
D
i
1.0
£
<
,
D
i
D
i
1
2
£
,
è
ø
ç
÷
ç
÷
æ
ö
U
total
C
1
T
1
...
C
n
T
n
U
n
D
i
,
(
)
£
+
+
=
Notes: It is common in control applications to set a task’s deadline to be prior to the end of its period. This is done to account for the transport delay.
Don’t worry about this formula. Just look up the utilization bound in Table 4-4 of the handbook. We will not go into any detail on preperiod deadlines or task switching. This is only made available to show that the situations can be analyzed using RMA.

## Slide 46: Schedulability with Interrupts
Interrupt processing can be inconsistent with rate-monotonic priority assignment.
  interrupt handler executes with high priority despite its period
  interrupt processing may delay execution of tasks with shorter periods
Effects of interrupt processing must be taken into account in schedulability model.
Question is: how to do that?
Notes: To this point we have assumed that all tasks run in rate monotonic order. Interrupt processing is common in real-time applications and often violates this assumption. Typically, interrupt processing is higher in priority than application-level processing. So although it may have a lower rate monotonic priority than an application-level task (i.e., it has a longer period), it will have a higher runtime priority and preempt the application-level tasks. To this point, the schedulability tests have not addressed this situation.
To clarify some definitions;
Runtime priority - the priority actually assigned to a task.
Rate monotonic priority - the priority of a task, if assigned according to its rate.
Runtime preemption - seizing of the CPU by a task with a higher runtime priority.
Rate monotonic preemption - delay of a task by a higher-rate task. (Generally when we use the term preemption, we mean rate monotonic preemption.)
Rate monotonic blocking (or rate monotonic priority inversion) - delay of a task by a lower-rate task. (In general, we will simply use the terms blocking and priority inversion for rate monotonic blocking and rate monotonic priority inversion.)
We will now explore how the basic rate monotonic schedulability model can be extended to account for interrupt processing.

## Slide 47: Example: Determining Schedulability with Interrupts
t3 is an interrupt handler
C T U
Task t1: 20 100 0.200
Task t2: 40 150 0.267
Task t3: 60 200 0.300
Task t4: 40 350 0.115
Notes: We will illustrate the way we address priority inversion with the above example.
Note that in this example, the interrupt has a lower rate monotonic priority than tasks t1 and t2.

## Slide 48: Example: Execution with Rate-Monotonic Priorities
t
1
t
2
t
3
t
4
0
100
200
300
400
Notes: This timeline shows how the tasks would execute under worst-case phasing if they ran in rate monotonic order. All tasks are clearly schedulable according to the “visual” CT test.
Unfortunately, this timeline is not how the tasks execute. Since t3 is an interrupt handler, it executes before the other tasks, causing additional delays to t1 and t2.

## Slide 49: Example: Execution with an Interrupt Priority
t
1
t
2
Interrupt
t
4
0
100
200
300
400
Notes: This timeline shows the actual execution order, where t3 is an interrupt handler and executes with a runtime priority that is higher than the other three tasks, in spite of its longer period. Notice the impact that the interrupt has on the completion time of the other three tasks. Both t1 and t2 are severely affected, being delayed by interrupt processing. However, t4 is not affected.
Execution is clearly inconsistent with the rate monotonic scheduling policy.

## Slide 50: Resulting Table for Example
Task (i) | Period (T) | Execution Time (C) | Priority (P) | Deadline (D)
t3 | 200 | 60 | Hardware (highest) | 200
t1 | 100 | 20 | High | 100
t2 | 150 | 40 | Medium | 150
t4 | 350 | 40 | Low | 350
Notes: Task Period Execution prior Deadline
Time
TskE 50 5 very high 0 6
TskR 24 2 High 0 24
Tsk1 100 20 Medium 20 100
Tsk2 150 40 Low 10 150
Tsk3 350 100 very low 0 350

## Slide 51: UB Test with Interrupt Priority
Test is applied to each task.
Determine effective utilization (fi) of each task ti using
j Hn
f
C
T
å
C
T
1
T
C
å
+
+
=
i
j
j
i
i
k
i
k H1
Preemption
from tasks that
can “hit” more than once
(with period less than Di)
Execution of
task under test
Preemption
from tasks that
can hit only once
(with period greater than Di)
Compare effective utilization against bound U(n).
  n = num(Hn) + 1
  num(Hn) = the number of tasks in the set Hn



## Slide 52: UB Test with Interrupt Priority: t3
For t3, no tasks have a higher priority:
  H = Hn = H1 = { }
f
0
å
C
T
0
å
+
+
=
3
3
3
Notnum(Hn) = 0; therefore, utilization bound is U(1).
Plugging in the numbers:
f
C
T
60
200
0.3
1.0
<
=
=
=
3
3
3

## Slide 53: UB Test with Interrupt Priority: t1
To t1, t3 has higher priority: H = {t3 }; Hn = { }; H1 = {t3 }
f
0
å
C
T
1
T
C
å
+
+
=
1
1
1
k
k=3
1
Note:
num(Hn) = 0; therefore, utilization bound is U(1).
Plugging in the numbers:
+
+
0.800 <
1.0
=
=
=
20
100
60
100
f
1
C
T
1
1
C
T
1
3

## Slide 54: UB Test with Interrupt Priority: t2
To t2: H = {t1,t3}; Hn = {t1}; H1 = {t3}.
f
å
C
T
1
T
C
å
+
+
=
2
2
2
k
k=3
2
C
T
j
j
j = 1
f
C
T
C
T
+
20
100
60
150
+
0.867 > 0.828
=
=
=
2
1
1
2
3
C
T
2
2
+
40
150
+
Note:
num(Hn) = 1; therefore, utilization bound is U(2).
Plugging in the numbers:

## Slide 55: UB Test with Interrupt Priority: t4
To t4: H = {t1, t2, t3}; Hn = {t1, t2, t3}; H1 = { }.
f
å
C
T
0
å
+
+
=
4
4
4
C
T
j
j
j = 1,2,3
f
C
T
C
T
+
20
100
+
=
=
4
1
1
3
3
C
T
2
2
+
C
T
4
4
+
40
150
+
60
200
350
+
40
= 0.882 > 0.756
Note:
num(Hn) = 3; therefore, utilization bound is U(4).
Plugging in the numbers:

## Slide 56: Exercise: Schedulability with Interrupts
Use the UB test to determine which tasks are schedulable
Given the following tasks:
Task (i) | Period (T) | Execution Time (C) | Deadline (D) | Priority (P)
τint | 6 | 2 | HW | 6
τ2 | 4 | 1 | High | 3
τ3 | 10 | 1 | Low | 10
Notes: 7
Since we are interested in worst-case behavior, tasks utilizations are always rounded up. For example, U2 = 40/150 = .2666... becomes .267 and U3 = 100/350 = .2857143... becomes .286.
In this example, since the total utilization is under the bound for three tasks, all tasks are guaranteed to meet their deadlines, even under worst-case conditions. An additional 24.7% CPU capacity is available for lower-priority tasks that have no deadline.
Remember that there are several assumptions associated with the utilization bound test:
Zero context switch overhead.
Deadlines are at end of period.
No interrupts are used.
Priorities are assigned in rate monotonic order.
Tasks do not interact with one another.
Tasks do not suspend themselves.

## Slide 57: Solution: Schedulability with Interrupts
0.334 < 1.0
U
1
£
(
)
Cint
Tint
+
U
1, .75)
£
(
C1
T1
Cint
T1
+
U
3)
£
(
C1
T1
Cint
Tint
+
C2
T2
0.250 + 0.500 = 0.750 = U(1, .75)
0. 334 + 0. 250 + 0.100 = 0.684 < 0.779
{H1}
{Hn}

## Slide 58: Classification of Scheduling Algorithms
All scheduling algorithms
static scheduling
(or offline, or clock-driven)
dynamic scheduling
(or online, or priority-driven)
fixed-priority
scheduling
dynamic-priority
scheduling
RMS
EDF

## Slide 59: Earliest Deadline First (EDF) Scheduling
Can be used to schedule periodic tasks
Uses dynamic priorities and preemptive scheduling
  Higher priority to task with earlier deadline
Example: 2-task set where each task is (C, T=D)  {(2, 4), (3, 7)}
Utilization U of task set {ti} for i = 1, …, n:
t1
t2

## Slide 60: EDF Schedulability Condition
Theorem: A task set is schedulable under EDF if and only if U ≤ 1.
Proof:
Assume that “overflow” occurs at time t2.
Let t1 be the latest time before t2 such that
  the processor is fully utilized in the interval [t1 , t2]
  only instances with deadlines before t2 executes in [t1 , t2]
If such a t1 cannot be found, then set t1 = 0.
Let Cd be the computational demand in [t1 , t2]
But an overflow implies that Cd > (t2 - t1) : a contradiction if U ≤ 1.
t1
t2

## Slide 61: Points to Note
If deadlines are shorter than periods, the necessary condition for schedulability under EDF is an open problem.
If U > 1, which task will first miss its deadline is unpredictable.

## Slide 62: Basic Theory: Where Are We?
We have shown how to handle
  task context switching time: include 2S in C
  Pre-period deadlines: change bound to U(n, Di)
  non-rate-monotonic priority assignments
We still must address
  task interactions
  aperiodic tasks
We still assume
  single processor
  priority-based scheduling
  a task does not suspend itself voluntarily
Notes: The schedulability model is now as complex as it will get. By adding blocking, as well as context switching and dormant time, we have extended the model to address the issues we will cover in this tutorial. We still have to cover task interactions through synchronization, which does not change the schedulability model but gives additional sources of blocking effects that must be included. Finally, we will add aperiodic tasks, which are handled by making them pseudo-periodic.
Remember that we still assume that all tasks run on a single CPU, that priority-based scheduling is used, and that tasks do not suspend themselves. However, later we will study a case in which priority-based scheduling is not used and look at its schedulability.

## Slide 63: Summary
Present basic theory for periodic task sets
Extend basic theory to include
  context switch overhead
  preperiod deadlines
  Interrupts
Consider task interactions:
  priority inversion
  synchronization protocols (time allowing)
Extend theory to aperiodic tasks:
  sporadic servers (time allowing)
Next Lecture:
Notes: 25
The approach that we will take with this tutorial is to start with very simple concepts and gradually build onto this foundation with more practical, real-world considerations.
We will first introduce the mechanics of RMA, applying the basic theory for independent, periodic tasks.
We will then extend the basic theory to include practical issues, such as context switch overhead, interrupts, and non-rate-monotonic priority assignments.
We will present a case study that incorporates the strategies covered and demonstrates the benefits of using RMA.
There will be exercises associated with some sections to practice the concepts discussed in those modules.
Next, as time allows, we will consider task interaction and aperiodic events, incorporating these issues into the analysis