## Slide 1: 18-349: Introduction to Embedded Real-Time Systems
Anthony Rowe
Electrical and Computer Engineering
Carnegie Mellon University
Lecture 15: Real-Time Synchronization

## Slide 2: Administrivia
Lab 3 out
Next Class Lab 3 Design Review
No Class Monday

## Slide 3: Today’s Lecture
Scheduler Implementation
Basic Priority Inheritance Protocol (BIP or PIP)
Priority Ceiling Protocol (PCP)
Highest Locker’s Priority Protocol (HLP)
Non-preemption Protocol (NPP)
Example

## Slide 4: RTOS Anatomy
thread_fork( function_ptr, int C_value, int T_value );
thread_wait_until_next_period(); // Absolute Wait
thread_wait_until( os_ticks ); // Relative Wait
kernel_main()
{
int stat;
stat=thread_fork( &my_task, 1, 6);
}
void my_task()
{
while(1)
{
do_work();
thread_wait_until_next_period( );
}
}

## Slide 5: Implementing RMS
OS Timer Tick (Jiffy)
τ1 = { 2, 5 }
τ2 = { 1, 6 }
τ1
τ2
System Time: 0
Run Queue -> τ1 (2,0) τ2 (1,0)
Waiting Queue ->
0
5
10
15
τ1
τ1
τ1
τ2
τ2
Budget
Became Runnable
τi = { C, T }

## Slide 6: Implementing RMS
OS Timer Tick (Jiffy)
τ1 = { 2, 5 }
τ2 = { 1, 6 }
τ1
τ2
System Time: 1
Run Queue -> τ1 (1,0) τ2 (1,0)
Waiting Queue ->
0
5
10
15
τ1
τ1
τ1
τ2
τ2
τi = { C, T }

## Slide 7: Implementing RMS
OS Timer Tick (Jiffy)
τ1 = { 2, 5 }
τ2 = { 1, 6 }
τ1
τ2
System Time: 2
Run Queue -> τ1 (0,0) τ2 (1,0)
Waiting Queue ->
0
5
10
15
τ1
τ1
τ1
τ2
τ2
τi = { C, T }

## Slide 8: Implementing RMS
OS Timer Tick (Jiffy)
τ1 = { 2, 5 }
τ2 = { 1, 6 }
τ1
τ2
System Time: 2
Run Queue -> τ2 (1,0)
Waiting Queue -> τ1 (2,5)
0
5
10
15
τ1
τ1
τ1
τ2
τ2
Becomes Runnable (last value + T)
τi = { C, T }

## Slide 9: Implementing RMS
OS Timer Tick (Jiffy)
τ1 = { 2, 5 }
τ2 = { 1, 6 }
τ1
τ2
System Time: 3
Run Queue -> τ2 (0,0)
Waiting Queue -> τ1 (2,5)
0
5
10
15
τ1
τ1
τ1
τ2
τ2
τi = { C, T }

## Slide 10: Implementing RMS
OS Timer Tick (Jiffy)
τ1 = { 2, 5 }
τ2 = { 1, 6 }
τ1
τ2
System Time: 3
Run Queue -> τ2 (0,0)
Waiting Queue -> τ1 (2,5)
0
5
10
15
τ1
τ1
τ1
τ2
τ2
τi = { C, T }

## Slide 11: Implementing RMS
OS Timer Tick (Jiffy)
τ1 = { 2, 5 }
τ2 = { 1, 6 }
τ1
τ2
System Time: 3
Run Queue ->
Waiting Queue -> τ1 (2,5), τ2 (1,6)
0
5
10
15
τ1
τ1
τ1
τ2
τ2
τi = { C, T }

## Slide 12: Implementing RMS
OS Timer Tick (Jiffy)
τ1 = { 2, 5 }
τ2 = { 1, 6 }
τ1
τ2
System Time: 4
Run Queue ->
Waiting Queue -> τ1 (2,5), τ2 (1,6)
0
5
10
15
τ1
τ1
τ1
τ2
τ2
τi = { C, T }

## Slide 13: Implementing RMS
OS Timer Tick (Jiffy)
τ1 = { 2, 5 }
τ2 = { 1, 6 }
τ1
τ2
System Time: 5
Run Queue -> τ1 (2,5)
Waiting Queue -> τ2 (1,6)
0
5
10
15
τ1
τ1
τ1
τ2
τ2
τi = { C, T }

## Slide 14: Implementing RMS
OS Timer Tick (Jiffy)
τ1 = { 2, 5 }
τ2 = { 1, 6 }
τ1
τ2
System Time: 6
Run Queue -> τ1 (1,5), τ2 (1,6)
Waiting Queue ->
0
5
10
15
τ1
τ1
τ1
τ2
τ2
τi = { C, T }

## Slide 15: Implementing RMS
OS Timer Tick (Jiffy)
τ1 = { 2, 5 }
τ2 = { 1, 6 }
τ1
τ2
System Time: 7
Run Queue -> τ1 (0,5), τ2 (1,6)
Waiting Queue ->
0
5
10
15
τ1
τ1
τ1
τ2
τ2
τi = { C, T }

## Slide 16: Implementing RMS
OS Timer Tick (Jiffy)
τ1 = { 2, 5 }
τ2 = { 1, 6 }
τ1
τ2
System Time: 7
Run Queue -> τ2 (1,6)
Waiting Queue -> τ1 (2,10)
0
5
10
15
τ1
τ1
τ1
τ2
τ2
τi = { C, T }

## Slide 17: Implementing RMS
OS Timer Tick (Jiffy)
τ1 = { 2, 5 }
τ2 = { 1, 6 }
τ1
τ2
System Time: 8
Run Queue -> τ2 (0,6)
Waiting Queue -> τ1 (2,10)
0
5
10
15
τ1
τ1
τ1
τ2
τ2
τi = { C, T }

## Slide 18: Implementing RMS
OS Timer Tick (Jiffy)
τ1 = { 2, 5 }
τ2 = { 1, 6 }
τ1
τ2
System Time: 9
Run Queue ->
Waiting Queue -> τ1 (2,10), τ2 (1,12)
0
5
10
15
τ1
τ1
τ1
τ2
τ2
τi = { C, T }

## Slide 19: Suspending by Spinning…
int thread_suspend()
{
volatile int tmp;
my_task -> status = TASK_WAITING;
do{
tmp=my_task -> status;
// Spin until the OS Jiffy fires…
} while( tmp == TASK_WAITING)
}

## Slide 20: Representing Time
Time is handled with a structure (not time_t 32-bit junk)
The “most standard” way of storing time in an RTOS is using the timespec structure
Used for absolute and relative time
// defined in time.h
struct timespec {
time_t tv_sec; // Seconds
long tv_nsec; // Nano-seconds
};

## Slide 21: Today’s Lecture
Scheduler Implementation
Basic Priority Inheritance Protocol (BIP or PIP)
Priority Ceiling Protocol (PCP)
Highest Locker’s Priority Protocol (HLP)
Non-preemption Protocol (NPP)
Example

## Slide 22: Priority Inversion
Ideally, under prioritized preemptive scheduling, higher priority tasks should immediately preempt lower priority tasks.
When lower priority tasks cause higher priority tasks to wait (e.g. the locking of shared data), priority inversion is said to occur.
It seems reasonable to expected that the duration of priority inversion (also called blocking time) should be a function of the duration of the critical sections.
Critical section:
  the duration of a task using a shared resource.

## Slide 23: Priority Inversion
Time
t1(H)
Critical Section
Executing
t2
t3
S1
S1
S1
S1
Notes: Basic Inheritance Protocol (BIP)
Execute the critical section at the priority of the highest-priority task being blocked.
Lock requests are always granted.
Higher-priority tasks may preempt the critical section as long as they do not try to lock the semaphore.

## Slide 24: Unbounded Priority Inversion
Time
t1(H)
Critical Section
Executing
t5
S1
S1
S1
S1
t4
t3
t2
Blocked!
Notes: Basic Inheritance Protocol (BIP)
Execute the critical section at the priority of the highest-priority task being blocked.
Lock requests are always granted.
Higher-priority tasks may preempt the critical section as long as they do not try to lock the semaphore.

## Slide 25: Priority Inversion
Delay to a task’s execution caused by interference from lower priority tasks is known as priority inversion.
Priority inversion is modeled by blocking time.
Identifying and evaluating the effect of sources of priority inversion is important in schedulability analysis.

## Slide 26: Sources of Priority Inversion
Synchronization and mutual exclusion
Non-preemptable regions of code
FIFO (first-in-first-out) queues

## Slide 27: Accounting for Priority Inversion
Recall that task schedulability is affected by
  preemption: two types of preemption
    can occur several times per period
    can only occur once per period
  execution: once per period
  blocking: at most once per period for each source
The schedulability formulas are modified to add a “blocking” or “priority inversion” term to account for inversion effects.

## Slide 28: How Real is Priority Inversion?
Mars Pathfinder experienced total system resets
Operating system used: WindRiver’s VxWorks
  Preemptive priority scheduling of threads
Pathfinder’s priority-based architecture
  High-priority thread managed the information bus
  Medium-priority thread ran a communications task
  Low-priority data-gathering thread used bus to publish data
  Bus access governed by mutex
What happened?
  High-pri task blocked, waiting for low-pri task to release mutex
  Interrupt would occur, causing med-pri task to be scheduled
  Watchdog timer would notice that high-pri task did not run for a while, and cause a total system restart
Notes: Vxworks had PCP disabled by default!

## Slide 29: Synchronization Protocols
No preemption
Basic priority inheritance
Highest locker’s priority
Priority ceiling
Each protocol prevents unbounded priority inversion.

## Slide 30: Basic Priority Inheritance Protocol
Let the lower priority task t3 use the highest priority of the higher priority tasks it blocks. In this way, the medium priority tasks can no longer preempt low priority task t3, which has blocked the higher priority tasks.
Priority inheritance is transitive.
  If A blocks B and B blocks C, A should execute at the priority of max(B,C).

## Slide 31: Basic Priority Inheritance Protocol (PIP)
Time
t1(H)
t4(L)
Critical Section
Executing
Blocked
t2: ( … P(S1) … V(S1) …)
t4: ( … P(S1) … V(S1) …)
t2
t3
S1 Locked
Ready
Ready
S1 unlocked
Attempt to lock S1 (blocked)
S1 unlocked
S1 Locked
B
B
Notes: Basic Inheritance Protocol (BIP)
Execute the critical section at the priority of the highest-priority task being blocked.
Lock requests are always granted.
Higher-priority tasks may preempt the critical section as long as they do not try to lock the semaphore.

## Slide 32: Deadlock: Using PIP
Time
t1(H)
S1 locked
Executing
Blocked
t1: ( … P(S1) … P(S2) … V(S2) … V(S1) …)
t2: ( … P(S2) … P(S1) … V(S1) … V(S2) …)
t2(M)
S1 Locked
S2 locked
S2 Locked
Attempt to lock S2 (blocked)
Attempt to lock S1 (blocked)
B
B
Notes: Necessary Conditions for Deadlock
-----------------------------------------------
Mutual Exclusion
Hold + Wait (Resource Holding)
No Preemption of resources
Circular Wait

## Slide 33: Example Of Chained Blocking (PIP)
Time
S1 locked
Executing
Blocked
t1: ( … P(S1) … P(S2) … V(S2) … V(S1) …)
t2: ( … P(S1) … V(S1) …)
t3: ( … P(S2) … V(S2) …)
S2 locked
B
t1(H)
t3(L)
t2(M)
S2 Locked
S2 unlocked
Attempt to lock S1
S1 unlocked
S1 Locked
S1 Locked
Attempt to lock S2
S2 Locked
B
B

## Slide 34: Properties of Basic Priority Inheritance
There will be no deadlock if there is no nested locks, or application level deadlock avoidance scheme such the ordering of resource is used.
Chained priority is fact of life. But a task is blocked at most by n lower priority tasks sharing resources with it, when there is no deadlock.
The priority inheritance protocol is supported in POSIX real time extensions.
  It is easy to implement
  it is supported by not only most RT OS vendors but also OS/2, Windows 95, Windows CE, AIX, HP/UX and Solaris.

## Slide 35: Blocking Term under PIP
Theorem: A higher-priority task can be blocked for at most one lower-priority critical section by each mutex
  Proof Sketch: Once a mutex has been released, it cannot be locked by any other lower-priority tasks
Theorem: A higher-priority task can be blocked for at most one (outermost) critical section of a lower-priority task
  Proof Sketch: Once a lower-priority task has exited a critical section, it can no longer block a higher-priority task until it completes.
If there are n lower-priority tasks and m distinct mutexes, a task can be blocked for no more than min(m, n) lower priority critical sections
  Assuming that deadlocks are avoided using other mechanisms

## Slide 36: Priority Ceiling Protocol
A priority ceiling is assigned to each mutex, which is equal to the highest priority task that may use this mutex.
A task can lock a mutex if and only if its priority is higher than the priority ceilings of all mutexes locked by other tasks.
If a task is blocked by a lower priority task, the lower priority task inherits its priority.

## Slide 37: Priority Ceiling Protocol (PCP)
C
S1 Locked
Ready
Ready
S1 unlocked
Attempt to lock S1 (blocked)
S1 unlocked
S1 Locked
time
t1(H)
t3
t4(L)
t2
t2: ( … P(S1) … V(S1) …)
t4: ( … P(S1) … V(S1) …)
Critical Section
Executing
Blocked
B
B
Ceiling
C
Notes: Priority Ceiling Protocol (PCP)
Basic Inheritance Protocol, plus a rule about when to grant lock requests.
  Ceiling: each semaphore is assigned a priority ceiling equal to the highest locker’s priority.
  Ceiling rule: a task cannot lock a free semaphore unless its priority is strictly greater than the “system” ceiling, which is the maximum ceiling of all semaphores currently locked by other tasks.
Block-at-most-once and deadlock-avoidance.

## Slide 38: Blocked At Most Once (PCP)
time
S1 locked
Executing
Ceiling
t1: ( … P(S1) … P(S2) … V(S2) … V(S1) …)
t2: ( … P(S1) … V(S1) …)
t3: ( … P(S2) … V(S2) …)
S2 locked
t1(H)
t2(M)
S2 unlocked
Attempt to lock S1
S1 Locked
Attempt to lock S1
S2 Locked
t3(L)
S2 Locked
S2 unlocked
S1 unlocked
S1 Locked
S1 unlocked
C
C

## Slide 39: Deadlock Avoidance: Using PCP
time
t1(H)
S1 locked
Executing
Ceiling
t1: ( … P(S1) … P(S2) … V(S2) … V(S1) …)
t2: ( … P(S2) … P(S1) … V(S1) … V(S2) …)
t2(M)
S1 Locked
S2 locked
S2 Locked
Attempt to lock S1
S1 Locked
S1 unlocked
S2 unlocked
S2 Locked
S2 unlocked
S1 unlocked
C
C

## Slide 40: Highest Locker’s Priority Protocol
time
t1(H)
t4(L)
Critical Section
Executing
Blocked
t2: ( … P(S1) … V(S1) …)
t4: ( … P(S1) … V(S1) …)
t2
t3
S1 Locked
Ready
Ready
S1 unlocked
B
B
B
Notes: Highest Locker’s Priority Protocol
Execute the critical section at the the priority of the highest-priority task that may lock the semaphore.
Lock requests are always granted.
Higher-priority tasks may preempt the critical section, but by definition they will not attempt to lock the semaphore.

## Slide 41: Non-Preemption Protocol
time
t1(H)
t4(L)
Critical Section
Executing
Blocked
t2: ( … P(S1) … V(S1) …)
t4: ( … P(S1) … V(S1) …)
t2
t3
S1 Locked
Ready
Ready
Ready
S1 unlocked
B
B
Notes: Nonpreemption Protocol
Do not allow preemption during execution of critical sections.
Lock requests are always granted.
Effectively, the critical section is executed at “infinite” priority.

## Slide 42: Summary of Synchronization Protocols
Protocol | Bounded Priority Inversion | Blocked for at most one critical section | Deadlock avoidance | Pessimism | Code Complexity
Basic priority inheritance protocol | Yes | No | No | low | hard
Priority Ceiling protocol | Yes | Yes2 | Yes | med | medium
Highest locker’s priority | Yes | Yes1 | Yes1 | medium | easy
Nonpreemptable critical sections | Yes | Yes1 | Yes1 | high | easy
1 Only if tasks do not suspend within critical sections
2 PCP is not affected if tasks suspend within critical sections

## Slide 43: Example

## Slide 44: (Conservative) Analysis for PCP

## Slide 45: Plugging in the numbers

## Slide 46: Summary
Real-Time Synchronization Protocols are required to prevent potentially unbounded priority inversion
Protocols available:
  Priority Inheritance Protocol
  Priority Ceiling Protocol
  Highest Locker’s Priority
  Non-preemption Protocol
Developed at Carnegie Mellon and widely supported by standards and products
Next Up: Memory Management
Notes: 15