## Slide 1: 18-349: Introduction to Embedded Real-Time Systems
Anthony Rowe
Electrical and Computer Engineering
Carnegie Mellon University
Lecture 17: Low-Power Embedded

## Slide 2: Administrivia
Lab 3 rolling along

## Slide 3: Overview
Why do we care about power?
Low-Power Scheduling
  Dynamic Voltage and Frequency Scaling
Rate Harmonized Scheduling
  Energy-Saving RHS
  Timer Coalescing

## Slide 4: Why do we care about power?

## Slide 5: Power Trend in Mobile Devices
year
Voice/Text/
SMS
Picture Message/
Narrowband Internet
Mobile
Multimedia
Multimedia
Message/
Broadband Internet
1990
2010
Power
Power Demand
Power Supply
(Energy Density)
The power supply & demand relationship is according to unpublished research by the Boston Consulting Group
Higher Bandwidth
Higher Computing
From phone to computing platforms
Notes: "According to unpublished research by the Boston Consulting Group, the amount of energy that a battery can store (its energy density) is growing by 8% a year. Mobile-device power consumption, meanwhile, is growing at more than three times this rate, as backlit colour screens, high-speed wireless networks and more powerful microprocessors draw ever-larger amounts of power."

## Slide 6: Important Note
The peak computing rate needed is much higher than the average throughput that must be sustained;
High performance is needed only for a small fraction of time, while for the rest of time, a low-performance, a low-power processor would suffice.

## Slide 7: Workload Profile
Time
Work load
Peak Computing Rate is needed
Average rate would suffice

## Slide 8: Motivations
The power consumption of CMOS circuits is given by P  CL * V2dd * f
f  (Vdd-Vth) / Vdd ; For a 0.25-m technology,   1.3-1.5
Energy = P * Delay  k * f 2/(-1)  k * f x
    Running a CPU at lower speed consumes less energy
Real-Time Tasks are required to complete at their deadline.
    Reducing the CPU speed to complete the task just before its deadline achieves the same performance but saves energy

## Slide 9: Issue of Operating Voltage/Frequency
Predominant device technology is CMOS
In CMOS, slower (faster) frequency means lower (higher) number of transitions
  Hence, lower power is consumed
Power is proportional to V2f
  P  Power
  V  Voltage
  f  Frequency
Can reduce unit computation energy by reducing frequency and voltage
Maximum gate delays inversely related to voltage
Applies to processors.
Can be applied to memory as well.
Check specifications carefully.

## Slide 10: Scaling Techniques
DFS: Dynamic Frequency Scaling
  Lower or increase clock frequency
  With lower frequency, the same amount of work (# of instructions to be executed) takes longer
  Hence, power may go down, but energy may remain the same
DVS: Dynamic Voltage Scaling
  Lower or increase clock voltage
  As frequency increases, higher voltage is required
  Conversely, as frequency is lowered, only a lower voltage is required
DVFS: Dynamic Voltage/Frequency Scaling
  Scale voltage up (down) when frequency is scaled up (down)
  Needs processors supporting software adjustable PLL, voltage regulator
    e.g., XScale, SpeedStep, PowerNow!, Crusoe, many many more…

## Slide 11: DVFS Example
Atmel ATmega1281

## Slide 12: DVS-example
Consider a task with a computation time 20 units.
Energy of Ti without DVS:
  E1 = K * 20 * F2.
Energy of Ti with DVS:
  E2 = K * 20 * (F/2)2.
We see that E2 = (E1)/4
Time taken = t1 (say)
Time taken = t2 = 2 * t1
Therefore, if we reduce the frequency we save energy but, we spend more time in performing the same computation

## Slide 13: Using DFS
“Static” DFS
Taskset: t1= (1, 5) t2 = (2, 10) t3 = (1, 10)
  U = 1/5 + 2/10 + 1/10 = 0.5
5
10
15
20
0
t1
t2
t3
10
15
t1
t1
t1
t2
t3
5
10
15
20
0
t1
t2
t3
15
t1
t1
t1
t2
t3
t2
t2
Before DFS
After DFS

## Slide 14: Simple DVS scheme handling RT-task
20@F
Frequency
F
20
30
time
20@(F/2)
Frequency
F
20
F/2
40
time
No DVS
DVS: Low workload
Inference:
DVS cannot be blindly applied to real-time embedded systems

## Slide 15: Overview
Why do we care about power?
Low-Power Scheduling
  Dynamic Voltage and Frequency Scaling
Rate Harmonized Scheduling
  Energy-Saving RHS
  Timer Coalescing

## Slide 16: Aside: Computing Battery Life
Batteries specified in Amp-Hours (AH) or milli Amp-Hour (mAH)
  Not really a measure of energy!
1AH (or 1000mA) means that the battery can provide 1 Amp of current for an hour or 1mA of current for 1000 hours at the nominal voltage
How do we use it?
  Compute your average current consumption ia
  Take battery capacity in AH and divide by ia
  This gives you total expected hours
Capacity is temperature and load dependent
AA is typically 2800mAH capacity

## Slide 17: Processor Energy States
Sleep
5uW
Idle
6mW
Active
30mW
10ms
6uS
1ms
6uS

## Slide 18: Power Modes of Microcontrollers
Power state | Power (mW) | Upward Transition Time
Active | 30 mW | n/a
Idle | 6 mW | 6 us
Sleep | 5 uW | 10 ms
Power Management: maximize the Sleep-time of processors
  given {Sleep, Idle, Active} modes of operation

## Slide 19: Simple RMS Example
0
5
10
15
20
25
30
35
40
45
50
55
60
65
70
75
80
85
90
95
100
105
110
1
2
Idle
Sleep
Csleep = 15
{5,35}
{5,50}
{ c, t }

## Slide 20: Example CPU parameters
Processor | Freq. (MHz) | Power Sleep (mW) | Power Idle (mW) | Power Active (mW) | Sleep to Idle (ms) | Idle to Active (us)
ATmega1281 | 8 | .016 | 6.6 | 23 | 12 | 6
Hitachi H8 | 8 | .00005 | 60 | 90 | 100 | 8
MSP430F5418 | 8 | 0.00033 | 0.0085 | 4 | 10 | 5
ST Cortex M3 | 20 | .0056 | 18.5 | 85 | 2 | 2
LPC2106 | 60 | .001 | 10 | 108 | 10 | 4
BF531 | 600 | .015 | 30 | 616 | 5 | 2

## Slide 21: RHS Problem Statement
Modern processors have support for different sleep modes
  Active (Most energy, full processing)
  Idle (Low energy, but no processing)
  Sleep (Lowest energy, oscillator off)
These states have a transition time penalty
  Active <-> Idle (fast)
  Idle <-> Sleep (slow due to oscillator spin-up)
Sometimes we can’t sleep because the transition time would be too long
  Can we batch task execution together to reduce transition overhead?

## Slide 22: Rate-Harmonizing Schedulers
Use a Harmonizing Base Period denoting when tasks are eligible to execute
  Tasks released as they normally would be released (only eligible after base period)
  Cluster task execution together whenever possible
  Maintain analyzable utilization bounds

## Slide 23
0
5
10
15
20
25
30
35
40
45
50
55
60
65
70
75
80
85
90
95
100
105
110
1
2
3
Idle
Sleep
RMS (Csleep =5)
{1,10}
{1,15}
{2,26}
{1,10}
{1,15}
{2,26}
1
2
3
Idle
Sleep
RHS (Csleep =5)
Base Harmonizing Period = 10

## Slide 24: What about the schedulability (RHS)?
Task sets are still feasible under basic rate harmonized scheduling if:
Exact schedulability condition:

## Slide 25: All idles appear to be gone…
{1,10}
{1,15}
{2,26}
1
2
3
Idle
Sleep
RHS (Csleep =5)
Base Harmonizing Period = 10
0
5
10
15
20
25
30
35
40
45
50
55
60
65
70
75
80
85
90
95
100
105
110
No, identical task set with Csleep = 7
1
2
3
Idle
RHS (Csleep =7)
0
5
10
15
20
25
30
35
40
45
50
55
60
65
70
75
80
85
90
95
100
105
110
Sleep
{1,10}
{1,15}
{2,26}

## Slide 26: Energy-Saving Rate-Harmonizing Scheduling
Create an Energy Saver task with
  period = rate-harmonizing period
  budget = sleep time required for the rate-harmonizing task

## Slide 27: Energy Saving RHS
1
2
3
Idle
RHS (Csleep =7)
0
5
10
15
20
25
30
35
40
45
50
55
60
65
70
75
80
85
90
95
100
105
110
Sleep
{1,10}
{1,15}
{2,26}
Energy-Saving RHS (Csleep =7)
1
2
3
Idle
Sleep
{1,10}
{1,15}
{2,26}
Energy Saver Task
Slack is merged together

## Slide 28: Properties of Energy Saving RHS
All Idle task slots become sleep!
We might not need all three CPU states
Energy Consumption is now very regular
  We can more accurately estimate lifetimes

## Slide 29: What about schedulability (ES-RHS)?
Only exact case condition

## Slide 30: How much energy can we save?
Task | C | T | U
1 | 1 | 20 | .050
2 | 1 | 25 | .040
3 | 1 | 26 | .038
4 | 1 | 28 | .035
5 | 1 | 32 | .031
6 | 2 | 50 | .04
7 | 2 | 67 | .029
8 | 3 | 91 | .033
9 | 9 | 100 | .090
Csleep = 10 ms
Tsleep = 20 ms
CPU = ATmega1281
RMS = 9.83 mW
ES-RHS = 6.5 mW
RHS saves 33%

## Slide 31: How much do we save in a real system?
Task | C | T | U
Link Layer | 1 | 20 | .050
Network Layer | 1 | 25 | .040
HF Sensor Sampling | 1 | 26 | .038
Mobile Node Service | 1 | 28 | .035
Diagnostic | 1 | 32 | .031
RMS = 2.38mW RHS = 2.00 mW
During the most active states we see a 16% savings on CPU energy

## Slide 32: Summary
Why do we care about power?
Low-Power Scheduling
  Dynamic Voltage and Frequency Scaling
Rate Harmonized Scheduling
  Energy-Saving RHS
  Timer Coalescing
Up Next: RT communication