## Slide 1: 18-349: Embedded Real-Time Systems Lecture 2: ARM Architecture
Anthony Rowe
Electrical and Computer Engineering
Carnegie Mellon University

## Slide 2: Basic Computer Architecture

## Slide 3: Memory Types
DRAM: Dynamic Random Access Memory
  Upside: very dense (1 transistor per bit) and cheap
  Downside: requires refresh and often slow
  Used as main memory
SRAM: Static Random Access Memory
  Upside: fast and no refresh required
  Downside: not so dense, not so cheap
  Often used for caches
EEPROM: Electronically Erasable Programmable Read-only Memory
  Used for bootstrapping
  Require wear-leveling

## Slide 4: Big Endian vs. Little Endian
How is a word, say, 0x1234567 stored in memory?

## Slide 5: Big Endian vs. Little Endian
Big-endian (big end first)
  Most significant byte of any multi-byte data field is stored at the lowest memory address
  Reading from left to right
  SPARC & Motorola
Little-endian (little end first)
  Least significant byte of any multi-byte data field is stored at the lowest memory address
  Reading from right to left instead
  Intel processors
Bi-endian (ARM, PowerPC, Alpha)

## Slide 6: CISC vs. RISC
RISC – Reduced Instruction Set Computers
CISC – Complex Instruction Set Computers
Different architectures for doing the same operations
Suppose you wanted to multiply two numbers in memory locations mem0 & mem1 and store the results back in mem0
  Same result but the complexity of operations and the number of steps used in the two cases differ

## Slide 7: CISC vs. RISC (1)
CISC | RISC
Example – Intel x86 chips | Examples – SPARC, PowerPC, ARM
Large number of instructions | Few instructions, typically less than 100
Variable-length instructions, instructions can range from 1-15 bytes | Fixed-length instructions, all instructions have the same number of bytes
Some instructions can have long execution times | No instruction with a long execution times execution time

## Slide 8: CISC vs. RISC (2)
CISC | RISC
Arithmetic and logical operations can be applied to memory and register operands | Arithmetic and logical operations only use register operands • Memory contents have to be loaded into registers first • Referred to as load/store architecture
Stack-intensive procedure linkage • Stack is used for procedure arguments and return values | Register-intensive procedure linkage • Registers used for procedure arguments and return values

## Slide 9: CISC vs. RISC (3)
CISC | RISC
Compact code size is typically small | Compiled code size is larger
More transistors = more power | Fewer transistors = less power

## Slide 10: ARM, Ltd.
Founded in November 1990
  Spun out of Acorn Computers based in U.K.
  ARM was originally Acorn RISC Machine; then, Advanced RISC Machine
Most widely used 32-bit instruction-set architecture in terms of volume
  6.1 billion ARM processors in 2010 up to 15 billion in 2015
  95% of all smartphones, 35% of digital TVs and set-top boxes
ARM architecture can be licensed, with licensees (former and/or current)
  AMD, Apple, Freescale, Microsoft, Nintendo, Xilinx, Qualcomm, TI, etc.
Companies design custom CPU cores with ARM instruction set
  Qualcomm’s Snapdragon, Apple’s A8, etc.
ARM Ltd. does not fabricate processors itself
  Also develops technologies to help with the design-in of ARM devices
  Software tools, boards, debug hardware, application software, buses, peripherals

## Slide 11: History of ARM’s Usage

## Slide 12: SoftBank Acquisition
Japanese multinational company
July 18th 2016
Purchased for £23.4 billion
Speculating on IoT market

## Slide 13: ARM Everywhere

## Slide 14: The ARM Family

## Slide 15: Different ARM Core Families
Cortex-A
  Application processors
  Single-core or multi-core
  Optional multimedia processing
  Optional floating-point units
  Smartphones, tablets, digital TVs, eBook readers
Cortex-R
  Deeply embedded real-time applications
  Low power, good interrupt behavior with good performance
  Automotive braking systems, printers, storage controllers
Cortex-M
  Cost-sensitive microcontrollers
  Fast, deterministic interrupt management
  Lowest possible power consumption
  Automotive airbags, tire-pressure monitoring, smart meters, sensors
Notes: Deterministic -> Can’t decide when an interrupt will happen, but we can guarantee how long it takes to service it

## Slide 16: Cortex-M Family

## Slide 17: Beyond Cortex
Break?

## Slide 18: ARM Data Sizes & Instructions
The ARM is a 32-bit RISC architecture
When used in relation to the ARM
  Byte means 8-bits
  Halfword means 16 bits (two bytes)
  Word means 32 bits (four bytes)
Most ARM processors implement two instructions sets
  32-bit ARM Instructions Set
  16-bit Thumb Instruction Set
Bi-endian
  Can be configured to view words stored in memory as either Big-endian or Little-Endian Format

## Slide 19: ARM is a RISC Architecture
A large array of uniform registers
A load/store model, where
  Operations operate only on register and not directly on memory
  All data must be loaded into registers before being used
  Result (in a register) can be further processed or stored to memory
A small number of addressing modes
  All load / store addresses are determined from register and isntruction fields
A uniform fixed-length instruction (32-bit)

## Slide 20: Programmer’s Model
ARM supports seven processor modes
  Characterized by specific behavior, privileges, associated registers
  Mode changes can be made under software control, or be caused by external interrupts or exception processing
Most applications execute in User mode
  Program cannot access certain protected resources
  Program cannot change mode without causing an exception
The 6 modes other then user mode are called privileged modes
  5 of these privileged modes are called exception modes
  The remaining one is called the System mode (same as User mode, but with access to protected resources)

## Slide 21: The Seven Modes
Notes: Supervisor - > “kernel”
Undefined -> Co processor that may undestand the instruction
System -> “root” mode

## Slide 22: Register Set (1)
ARM has a total of 37 registers all of which are 32-bit
  30 general-purpose registers
  1 dedicated program counter (pc)
  1 dedicated current program status register (cpsr)
  5 dedicated saved program status registers (spsr)
In any mode, only a subset of these 37 registers are visible
  The hidden registers are called banked registers
  The current processor-mode governs which registers are visible

## Slide 23: Register Set (2)
r0 through r7: Eight general-purpose registers that are always available, no matter which mode you’re in (8)
r8 through r12: Five general-purpose registers that are common to all processor modes other than fiq mode (5)
r8_fiq through r12_fiq: Five registers that replace the normal r8-r12 when the processor is in fiq mode (5)
Special-purpose registers
  r13 (stack pointer): Same for System and User mode, otherwise, r13_fiq, r13_svc, r13_abt, r13_irq, r13_und (6)
  r14 (link register): Same for System and User mode, otherwise, r14_fiq, r14_svc, r14_abt, r14_irq, r14_und (6)
  r15 (program counter): A unique one across all modes (1)
Notes: R14 Link Register -> Keeps track of where you branched from for a conditional

## Slide 24: Register Set (3)
Status registers
  cpsr (current program status register): Holds current status of processor, including its mode (1)
  spsr (saved program status register): Holds processor status information before program changes into an exception mode, r13_fiq, r13_svc, r13_abt, r13_irq, r13_und (5)

## Slide 25: Register Set (4)
1
2
3
4
5
6
7
8
9
10
11
12
13
19
20
14
15
16
17
18
21
22
23
24
25
26
27
28
29
30
31
32
33
34
35
36
37
Notes: 6 different R13 registers

## Slide 26: Banked Registers
Banking of registers implies
  The specific register depends not only on the number (r0,r1,…,r15) but also on the processor mode
Values stored in banked registers are preserved across mode changes
Example: Assume that the processor is executing in User Mode
  In User mode, assume that the processor writes 0 in r0 and 8 in r8
  Processor now changes to fiq mode
    In FIQ mode, the value of r0 is __________
    If processor now overwrites both r0 and r8 with 1 in fiq mode and changes back to user mode
      The new value stored in r0 (user mode) is _____________
      The new value stored in r8 (user mode) is _____________
Notes: In FIQ r0 is 0 (not banked)
New r0 is 1 (not banked)
New r8 is 8 (from original)

## Slide 27: Register Set in User Mode

## Slide 28: Register Set in fiq Mode
Notes: FIQ with extra registers to be faster
FIQ is not interruptible

## Slide 29: Thumb Mode
Thumb is a 16-bit instruction set
  Optimized for code density from C code (~65% of ARM code size)
  Improved performance from narrow memory
  Subset of the functionality of the ARM instruction set
Core has additional execution state – Thumb
  Switch between ARM and Thumb using BX instruction
For most instructions generated by compiler:
  Conditional execution is not used
  Source and destination registers identical
  Only Low registers used
  Constants are of limited size
  Inline barrel shifter not used

## Slide 30: The CPSR (1)
Current Program Status Register (cpsr) is a dedicated register
Holds information about the most recently performed ALU operations
Controls the enabling and disabling of interrupts (both IRQ and FIQ)
Sets the processor operating mode
Sets the processor state

## Slide 31: The CPSR (2)
cpsr has two important pieces of information
  Flags: contains the condition flags
  Control: contains the processor mode, state and interrupt mask bits
All fields of the cpsr can be read/written in privileged modes
  Only the flag field of cpsr can be written in User mode, all fields can be read in User mode

## Slide 32: The CPSR (3)
Interrupt Disable bits
  I = 1: Disables IRQ
  F = 1: Disables FIQ
T Bit
  T = 0: Processor in ARM state
  T = 1: Processor in Thumb state
Mode bits
  Specify the processor mode
When exceptions occur cpsr gets copied to the corresponding spsr_<mode> register for storage

## Slide 33: The CPSR (4)
Will represent this as nzcvqift_mode
Upper case letters will indicate that a certain bit has ben set
Examples
  nzcvqiFt_USER: FIQs are masked and the processor is executing in user mode
  nzCvqift_SVC: Carry flag is set and the processor is executing in supervisor mode
Notes: N – negative
Z – Zero
C – Carry
V - Overflow

## Slide 34: Exceptions vs. Interrupts
Term exception and interrupt are often confused!
Exception usually refers to an internal CPU event such as
  Floating point overflow
  MMU fault (e.g., page fault)
  Trap (SWI)
Interrupt usually refers to an external I/O event such as
  I/O device request
  Reset
In the ARM architecture manuals, the two terms are mixed together and are considered interchangeable

## Slide 35: ARM Exceptions
Exception | Mode | Description
Reset | Supervisor | Occurs when the processor􏰀s reset button is asserted. This exception is only expected to occur for signaling power up or for resetting the processor. A soft reset can be achieved by branching to reset vector 0x00000000 or letting the watchdog timer expire
Undefined Instruction | Undef | Occurs if neither the processor, nor any of the coprocessors, recognize the currently executing instruction
Software Interrupt | Supervisor | This is a user-defined synchronous interrupt. It allows a program running in the User mode to request privileged operations (for example an RTOS function) that run in Supervisor mode
Prefetch Abort | Abort | Occurs when a processor attempts to execute an instruction that was not fetched, because the address was illegal
Data Abort | Abort | Occurs when a data transfer instruction attempts to load or store data at an illegal address
IRQ | IRQ | Occurs when the processor􏰀s external interrupt request pin is asserted and the I bit in the cpsr is clear
FIQ | FIQ | Occurs when the processor􏰀s external fast interrupt request pin is asserted and the I (F-bit???) bit in the cpsr is clear

## Slide 36: ARM Exception Handling (1)
Exception Handler
  Most exceptions have an associated software exception handler that executes when that particular exception occurs
Exception modes and registers
  Handling exceptions changes program from user to non-user mode
  Each exception handler has access to its own set of registers
    Its own r13 (stack pointer)
    Its own r14 (link register)
    Its own spsr (Saved Program Status Register)
  Exception handlers must save (restore) other registers on entry (exit)

## Slide 37: ARM Exception Handling (2)
Where is the is exception handler located?
Vector table
  Reserved area of 32 bytes at the end of the memory map (starting at address 0x0)
  One word of space for each exception type
  Contains a Branch or Load PC instruction for the exception handler

## Slide 38: ARM Exception Handling (3)
When an exception occurs, the ARM processor:
  Copies cpsr into spsr_<mode>
  Sets appropriate cpsr bits
    Change to ARM state
    Change to exception mode
    Disable interrupts (if appropriate)
  Stores the return address in lr_<mode>
  Sets pc to vector address
To return, exception handler needs to:
  Restore cpsr from the spsr_<mode>
  Restore pc from lr_<mode>

## Slide 39: Simultaneous Exceptions?

## Slide 40: Why Exceptions?
Functionality that would otherwise not be possible
  Memory or Data Abort can be used to implement Virtual Memory
SWI allows for system calls
Undefined exceptions can be used to provide software emulation of coprocessor when the coprocessor is not physically present or could be used for special purpose instruction set extensions
  If an unknown instruction is reached the processor changes to Undefined mode and executes the Undefined Instruction exception handler
  In the exception handler, the coprocessor functionality can be provided in software (or the functionality provided by the enhanced instrucionts can be provided in software)

## Slide 41: Summary
What is an ARM?
  CISC vs RISC
  ARM family
  Memory
ARM Architecture from a programmer’s viewpoint
  Processor modes
  General purpose registers
  Special purpose registers
  Exception handling
Next Time: Deeper into ARM ASM