## Slide 1: 18-349: Introduction to Embedded Real-Time Systems Lecture 3: ARM ASM
Anthony Rowe
Electrical and Computer Engineering
Carnegie Mellon University

## Slide 2: Lecture Overview
Exceptions Overview (Review)
Pipelining
ARM ASM Introduction
  Move operations
  Arithmetic operations
  Logical operations
  Comparison operations
  Multiply operations
  Conditionals

## Slide 3: Reminder: ARM Register Set

## Slide 4: Control Flow
Processors do only one thing:
  From startup to shutdown, a CPU simply reads and executes (interprets) a sequence of instructions, one at a time
  This sequence is the CPU’s control flow (or flow of control)
<startup>
inst1
inst2
inst3
…
instn
<shutdown>
Physical control flow
Time

## Slide 5: Exceptions
An exception is a transfer of control to supervisory mode in response to some event (i.e., change in processor state)
Examples:
  div by 0, arithmetic overflow, page fault, I/O request completes, Ctrl-C
User Process
OS
exception
exception processing
by exception handler
return to I_current
return to I_next
abort
event
I_current
I_next

## Slide 6: The Vector Table
Reserved area of 32 bytes at the end of the memory map
  Placed at address 0x0
One word of space for each exception type
Contains a Branch or Load pc instruction for the exception handler
Notice that the FIQ exception-handler is at the end of the vector table – why?
FIQ
IRQ
(Reserved)
Data Abort
Prefetch Abort
Software Interrupt
Undefined Instruction
Reset
0x1C
0x18
0x14
0x10
0x0C
0x08
0x04
0x00
Notes: FIQ at end so that you can put code there without needing to branch!

## Slide 7: The Vector Table
0
1
2
...
n-1
Each type of event has a unique exception number k
k = index into exception table (a.k.a. interrupt vector)
Handler k is called each time exception k occurs
Exception
Table
code for
exception handler 0
code for
exception handler 1
code for
exception handler 2
code for
Fastest exception handler n-1
...
Exception
numbers

## Slide 8: Exception Handling
When an exception occurs, the ARM:
  Copies cpsr into spsr_<mode>
  Sets appropriate cpsr bits
    Change to ARM state
    Change to exception mode
    Disable interrupts (if appropriate)
  Stores the return address in lr_<mode>
  Sets pc to vector address
To return, exception handler (the code you write) needs to:
  Restore cpsr from spsr_<mode>
  Restore pc from lr_<mode>
  Handle the general-purpose (gp) registers appropriately
FIQ
IRQ
(Reserved)
Data Abort
Prefetch Abort
Software Interrupt
Undefined Instruction
Reset
0x1C
0x18
0x14
0x10
0x0C
0x08
0x04
0x00

## Slide 9: Example: User to Supervisor
Your program is initially in User mode
When the processor executes the SWI instruction, the ARM processor does the following for you automatically:
  Copies cpsr into spsr_svc
  Sets appropriate cpsr mode bits to 10011 (svc mode)
    Disables IRQs
  Stores return address (pc – 4) in lr_svc
  Sets pc to vector address 0x08
To return, exception handler (the code you have to write) needs to:
  Restore cpsr from spsr_svc (cpsr now has mode bits 10000 = usr mode)
  Restore pc from lr_svc
In Supervisor mode, a single instruction can be used to cause the SPSR for the current mode to be copied into CPSR while copying lr into pc
  MOVS pc, lr

## Slide 10: Peak at an Exception Handler
; ARM processor has already done its part
S_Handler
  STMFD sp!, {r0­r12, lr} ; store user's gp registers and lr_svc
  MOV r1, sp ; ignore for now
  LDR r0, [lr, #­4] ; ignore for now
  BIC r0,r0,#0xff000000 ; ignore for now
  BL C_SWI_handler ; ignore for now
  LDMFD sp!, {r0­r12, lr} ; unstack user's registers and lr_svc
  MOVS pc, lr ; return from handler

## Slide 11: Instruction Cycle
Two Steps:
  Fetch
  Execute

## Slide 12: The Fetch Cycle
Program Counter (PC)
  Holds address of next instruction that the processor should fetch
So, what happens?
  Processor fetches instruction from the memory location that the PC points to
  Processor then increments PC
    Unless specified otherwise
    Sometimes, an offset added depending on processor architecture
Instruction loaded into Instruction Register (IR)
  Processor interprets instruction and performs required actions

## Slide 13: The Execute Cycle
Processor-memory interactions
  Data transferred between CPU and main memory
Processor-I/O interactions
  Data transferred between CPU and I/O device
Data processing
  Some arithmetic or logical operation performed on data
Control action
  Alteration of sequence of operations
    Example: Branch to subroutine
Combination of the above

## Slide 14: Pipelining
Technique where multiple instructions are overlapped in execution
Each stage completes a part of the execution in parallel
Pipelining does not decrease/increase the amount of time taken for any single instruction to execute
Pipelining increases throughput, i.e., number of instructions exiting the pipeline in unit time
Source: http://cse.stanford.edu/class/sophomore-college/projects-00/risc/pipelining/

## Slide 15: Pipelining Stages
Processors can vary in the number of pipeline stages
Often some combination or extension of the following steps
  Fetch instructions from memory
  Decode the instruction
  Execute the instruction or calculate an address
  Access an operand in data memory
  Write the result into a register

## Slide 16: Issues in Pipelining
Length of the pipeline depends on the length of the longest step
  Pipeline rate limited by slowest pipeline stage
Because RISC instructions are simpler than CISC, they lend themselves better to pipelining
  RISC instructions are often the same length and can be fetched in one operation (ideally in 1 clock cycle)
OK, nothing is ever that simple or ideal
  Data dependencies: Instruction depends on the output value of a previous instruction; value might not yet be ready because that previous instruction is also somewhere (although ahead of the current one) in the pipeline
  Branch instructions: Next instruction to be executed is decided based on the result of executing another instruction; branch can be conditional on an instruction that has not even made it through the pipeline as yet
  Pipeline is stalled; empty instructions (bubbles) inserted into the pipeline

## Slide 17: Traditional ARM Pipeline
ARM traditionally employed a 3-stage pipeline with the following stages
  Fetch: instruction fetched from memory
  Decode: instruction is decoded
  Execute: instruction is executed
When processor is executing simple data processing instructions the pipeline enables one instruction to be completed every clock cycle
fetch decode execute
time
3
2
1
fetch decode execute
fetch decode execute

## Slide 18: Pipeline Changes for ARM9TDMI

## Slide 19: Pipeline changes for ARM10/11

## Slide 20: The ARM Assembly Language
ARM instructions can be broadly classified as
  Data Processing Instructions: manipulate data within the registers
  Branch Instructions: changes the flow of instructions or call a subroutine
  Load-Store Instructions: transfer data between registers and memory
  Software Interrupt Instruction: causes a software interrupt
  Program Status Instructions: read/write the processor status registers
All instructions can access r0-r14 directly
Most instructions also allow use of the pc
Specific instructions to allow access to cpsr and spsr

## Slide 21: ARM Instruction Set Format

## Slide 22: Data Processing Instructions
Manipulate data within registers
  Move operations
  Arithmetic operations
  Logical operations
  Comparison operations
  Multiply operations
Appending the S suffix for an instruction, e.g, ADDS
  Signifies that the instruction’s execution will update the flags in the cpsr

## Slide 23: Typical Data Processing Instruction
Operation – Specifies the instruction to be performed
Cond – specify the optional conditional flags which have to be set under which to execute the instruction
  Almost all ARM instructions can be conditionally executed
S bit – Signifies that the instruction updates the conditional flags
Rd – Specifies the destination register
Rn – Specifies the first source operand register
ShifterOperand2 – Specifies the second source operand
  Could be a register, immediate value, or a shifted register/immediate value
Some data processing instructions may not specify the destination register or the source register
<Operation>
<Cond>
{S}
Rd
Rn
ShifterOperand2

## Slide 24: Data Processing Instructions
Consist of :
  Arithmetic: ADD ADC SUB SBC RSB RSC
  Logical: AND ORR EOR BIC
  Comparisons: CMP CMN TST TEQ
  Data movement: MOV MVN
These instructions only work on registers, NOT memory

## Slide 25: Move Instruction
MOV moves a 32-bit value into a register
MVN moves the NOT of the 32-bit value into a register
PRE
r5 = 5
r7 = 8
MOV r7, r5
POST
r5 = 5
r7 = 5
Notes: R5 = r7 = 5

## Slide 26: The ARM Barrel Shifter
Data processing instructions are processed within the ALU
ARM can shift the 32-bit binary pattern in one of the source registers left or right by a specific number of positions before the value enters the ALU
Can achieve fast multiplies or division by a power of 2
Data-processing instructions that do not use the barrel shifter
  MUL (multiply)
  CLZ (count leading zeros)
  QADD (signed saturated 32-bit add)
Rn
Rm
Rd
Result N
Pre-processing
No pre-processing
Arithmetic and Logic
Unit (ALU)

## Slide 27: Using the Barrel Shifter
LSL shifts bits to the left, and is similar to the C-language operator <<
PRE
r5 = 5
r7 = 8
MOV r7, r5, LSL #2
POST
r5 = 5
r7 = 20
r7 = r5 * 4 = (r5 << 2)

## Slide 28: Updating the Condition Flags
The S suffix indicates that the cpsr should be updated
PRE cpsr = nzcvqiFt_USER
r0 = 0x00000000
r1 = 0x80000004
MOVS r0, r1, LSL #1
POST cpsr = nzCvqiFt_USER
r0 = 0x00000008
r1 = 0x80000004
Hint: 32-bit version of 0x80000004 is
1000 0000 0000 0000 0000 0000 0000 0100
Notes: r0 = 0x00000008, r1 = 0x80000004, cpsr has C flag also set
V flag does not get set since the specs for MOV instruction only allow C and Z flags to be affected
Assume 3 bit numbers
Carry but no overflow when you do -2 (110)+-2(110) = -4 ( 1100)
Overflow but no carry when you do 2 (010) + 2 (010) = -4 (100)
If the problem is changed to MOVS r0, r1, LSL #2 then no Carry is generated. Think of Carry bit in an operation MOV Rd, Rm, ShiftValue as Rm[32-ShiftValue] as long as ShiftValue > 0 (otherwise Carry bit is the same as what it was before).

## Slide 29: Arithmetic Operations
Operations are:
  ADD operand1 + operand2 ; Add
  ADC operand1 + operand2 + carry ; Add with carry
  SUB operand1 ‐ operand2 ; Subtract
  SBC operand1 ‐ operand2 + carry ‐1 ; Subtract with carry
  RSB operand2 ‐ operand1 ; Reverse subtract
  RSC operand2 ‐ operand1 + carry ‐ 1 ; Revers sub with carry
Syntax:
  <Operation>{<cond>}{S} Rd, Rn, Operand2
Examples
  ADD r0, r1, r2
  SUBGT r3, r3, #1
  RSBLES r4, r5, #5
Notes: {S} for updating condition flags

## Slide 30: Arithmetic Instructions
Subtract
PRE r0 = 0x00000000
r1 = 0x00000002
r2 = 0x00000001
SUB r0, r1, r2
POST r0 = 0x00000001
r1 = 0x00000002
r2 = 0x00000001
Addition
PRE r0 = 0x00000000
r1 = 0x00000005
ADD r0, r1, r1, LSL #1
POST r0 = 0x0000000f
r1 = 0x00000005
Notes: Part 1: r0 = 0x00000001, r1 and r2 unchanged
Part 2: Write r1 as 0000 0000 0000 0000 0000 0000 0000 0101
This value left-shifted by 1 is 0000 0000 0000 0000 0000 0000 0000 1010 = 0xoa
Add r1 back to this: r1 + left-shifted r1 = 0x05 + 0x0a = 0x0f
Final: r0 = 0x0000000f, r1 = 0x00000005

## Slide 31: Logical Operations
Operations are:
  AND operand1 AND operand2 ; and
  EOR operand1 EOR operand2 ; xor
  ORR operand1 OR operand2 ; or
  ORN operand1 NOR operand2 ; or negative (nor)
  BIC operand1 AND NOT operand2 ; bit clear
Syntax:
  <Operation>{<cond>}{S} Rd, Rn, Operand2
Examples
  AND r0, r1, r2
  BICEQ r2,r3 #7
  EORS r1,r3,r0
Notes: {S} for updating condition flags

## Slide 32: Logical Instructions
Bitwise logical operations on two source registers
AND, ORR, EOR, BIC
Logical OR
PRE r0 = 0x00000000
r1 = 0x02040608
r2 = 0x10305070
ORR r0, r1, r2
POST r0 = 0x12345678
r1 = 0x02040608
r2 = 0x10305070
Logical bit clear (BIC)
PRE r1 = 0b1111
r2 = 0b0101
BIC r0, r1, r2
POST r0 = 0b1010
r1 = 0b0101
r2 = 0b0101
Every binary 1 in r2 clears a corresponding bit location in r1
Notes: BIC = Bit Clear

## Slide 33: Multiply Instructions
Multiple a pair of registers and optionally add (accumulate) the value stored in another register
  MUL Rd, Rm, Rs Rd = Rm*Rs
  MLA Rd, Rm, Rs, Rn Rd = Rm*Rs + Rn
Special instructions called long multiplies accumulate onto a pair of registers representing a 64-bit value
  SMLAL, SMULL, UMLAL, UMUL
PRE r0 = 0x00000000 MUL r0, r1, r2 POST r0 = 0x04
r1 = 0x00000002 r1 = 0x02
r2 = 0x00000002 r2 = 0x02

## Slide 34: Conditional Execution
Most instruction sets only allow branches to be executed conditionally
However ARM reuses the condition evaluation hardware to effectively increase number of instructions
  All instructions have a field to determine if they should be conditionally executed
  Non-executed instructions consume 1 cycle
This removes many of the needs for branches, which stall the pipeline (at least 3 refill cycles)

## Slide 35: The Condition Field

## Slide 36: Conditional Mnemonics
Not equal
Unsigned higher or same
Unsigned lower
Minus
Equal
Overflow
No overflow
Unsigned higher
Unsigned lower or same
Positive or Zero
Less than
Greater than
Less than or equal
Always
Greater or equal
EQ
NE
CS/HS
CC/LO
PL
VS
HI
LS
GE
LT
GT
LE
AL
MI
VC
Suffix/Mnemonic
Description
Z=0
C=1
C=0
Z=1
Flags tested
N=1
N=0
V=1
V=0
C=1 & Z=0
C=0 or Z=1
N=V
N!=V
Z=0 & N=V
Z=1 or N=!V

## Slide 37: Comparison Instructions
The only effect of comparison is to update the condition flag. So now “S bit” needed.
Operations are:
  CMP operand1 - operand2 ; Compare
  CMN operand1 + operand2 ; Compare Negative
  TST operand1 ANDoperand2 ; Test
  TEQ operand1 EOR operand2 ; Test equivalence
Syntax:
  <Operation>{<cond>} Rn, Operand2
Examples
  CMP r0, r1
  TSTEQ r2, #5

## Slide 38: Comparison Instructions
Compare or test a register with a 32-bit value
  CMN, CMP, TEQ, TST;
Outcome: Registers under comparison are not affected; cpsr updated
  Example: CMP x,y sets cpsr flags based on results of x-y (subtract)
  Example: TST x,y sets cpsr flags based on results of x&y (logical AND)
Do not need the S suffix
PRE cpsr = nzcvqiFt_USER
r0 = 4
r9 = 4
CMP r0, r9
POST cpsr = nZcvqiFt_USER
r0 = 4
r9 = 4
Notes: Cpsr nZcvqiFt_USER
Template: Instruction Rn, N
CMN – flags set based on Rn + N
CMP – flags set based on Rn – N
TEQ – flags set based on Rn ^ N (logical XOR)
TST – flags set based on Rn & N

## Slide 39: Branch Instructions
To change the flow of execution or to call a routine
Supports subroutine calls, if-then-else structures, loops
Change of execution forces the pc to point to a new address
Four different branch instructions on the ARM
  B{<cond>} label
  BL{<cond>} label
  BX{<cond>} Rm
  BLX{<cond>} label | Rm
Notes: B = branch
BL = branch with link (Add PC+4 to R14)
BX = Branch exchange (Branch back from R14)
BLX = branch exchange with link

## Slide 40: Value of Conditional
This improves code density and performance by reducing the number of forward branch instructions
  if (x != 0) CMP r3,#0 a = b+c; BEQ skip else ADD r0,r1,r2
  a = b–c; B afterskip
  skip
  SUB r0, r1, r2
  afterskip
CMP r3,#0 ADDNE r0,r1,r2
SUBEQ r0,r1,r2

## Slide 41: Examples of Conditional Execution
Use a sequence of several conditional instructions
  if (a==0) x=1;
    CMP r0,#0 MOVEQ r1,#1
Set the flags, then use various condition codes
  if (a==0) x=0; if (a>0) x=1;
    CMP r0,#0 MOVEQ r1,#0 MOVGT r1,#1
Use conditional compare instructions
  if (a==4 || a==10) x=0;
    CMP r0,#4 CMPNE r0,#10 MOVEQ r1,#0

## Slide 42: Single Register Data Transfer
ARM is based on a “load/store” architecture
  All operands should be in registers
  Load instructions are used to move data from memory into registers
  Store instructions are used to move data from registers to memory
  Flexible – allow transfer of a word or a half-word or a byte to and from memory
  LDR/STR Word
  LDRB/STRB Byte
  LDRH/STRH Halfword
  LDRSB Signed byte load
  LDRSH Signed halfword load
Syntax:
  LDR{<cond>}{<size>} Rd, <address>
  STR{<cond>}{<size>} Rd, <address

## Slide 43: LDR and STR
LDR and STR instructions can load and store data on a boundary alignment that is the same as the datatype size being loaded or stored
LDR can only load 32-bit words on a memory address that is a multiple of 4 bytes – 0, 4, 8, and so on
LDR r0, [r1]
  Loads register r0 with the contents of the memory address pointed to by register r1
STR r0, [r1]
  Stores the contents of register r0 to the memory address pointed to by register r1
Register r1 is called the base address register

## Slide 44: LDR/STR Example
The memory location to be accessed is held in a base register
  STR r0, [r1] ; Store contents of r0 to location pointed
  ; to by contents of r1.
  LDR r2, [r1] ; Load r2 with contents of memory location
  ; pointed to by contents of r1

## Slide 45: Addressing Modes (1-4)
ARM provides three addressing modes
  Preindex with writeback
  Preindex
  Postindex
Preindex mode useful for accessing a single element in a data structure
Postindex and preindex with writeback useful for traversing an array

## Slide 46: Addressing Modes (2-4)
Preindex
  Same as preindex with writeback, but does not update the base register
  Example: LDR r0, [r1, #4]
Preindex with writeback
  Calculates address from a base register plus address offset
  Updates the address in the base register with the new address
  The updated base register value is the address used to access memory
  Example: LDR r0, [r1, #4]!
Postindex
  Only updates the base register after the address is used
  Example: LDR r0, [r1], #4

## Slide 47: Addressing Modes (3-4)
Preindexing with writeback
LDR r0, [r1, #4]!
POST r0 =
r1 =
PRE r0 = 0x00000000
r1 = 0x00009000
mem32[0x00009000] = 0x01010101
mem32[0x00009004] = 0x02020202
Preindexing
LDR r0, [r1, #4]
POST r0 =
r1 =
Postindexing
LDR r0, [r1], #4
POST r0 =
r1 =
0x02020202
0x00009004
0x02020202
0x00009000
0x01010101
0x00009004

## Slide 48: Addressing Modes (4-4)
Address <address> accessed by LDR/STR is specified by
  A base register plus an offset
Offset takes one of the three formats
  Immediate: offset is a number that can be added to or subtracted from the base register
  Example: LDR r0,[r1, #8]; r0 b mem[r1+8]
  LDR r0,[r1, #-8]; r0 b mem[r1-8]
  Register: offset is a general-purpose register that can be added to or subtracted from the base register
  Example: LDR r0,[r1, r2]; r0 b mem[r1+r2]
  LDR r0,[r1, -r2]; r0 b mem[r1-r2]
  Scaled Register: offset is a general-purpose register shifted by an immediate value and then added to or subtracted from the base register
  Example: LDR r0,[r1,r2, LSL #2]; r0 b mem[r1+4*r2]

## Slide 49: Summary
Exceptions
  Vector Table
Pipelining
  What is it?
  Why do we do it?
ARM ISA Introduction
Next Lecture
  Addressing Modes (reviewed) and Block Data Transfer
  Stack
  Memory Mapped IO