## Slide 1
Sathish Gopalakrishnan
Electrical and Computer Engineering
The University of British Columbia
Real-Time Communication

## Slide 2: Outline
Real-time communications
  Traffic and network models
  Properties of networks
    Throughput, delay and jitter
  Congestion and loss
Examples
  Controller area networks
  Ethernet

## Slide 3: Real-Time Communications
Digital data communications
  One would like fast delivery, but not at the expense of reliability
    E.g. web browsing, e-mail, file transfer, twitter, etc.
  These applications are often referred to as elastic applications
    i.e. time can be “dilated”
Real-time data communications
  Timely delivery may deemed to be more desirable than reliable delivery
  Different levels of priority may be associated with applications
  Examples:
    Anti-lock braking in a car
    “Fly-by-wire” systems in a modern aircraft
    Skype internet telephony and IPTV (TV using the Internet Protocol)
      drop delayed packets

## Slide 4: Real-Time Traffic Categories
Packet-switched traffic falls into two categories:
  Synchronous periodic messages
    Produced and consumed in a continual basis, according to some schedule
      Generally require some performance guarantee
      Can be generated by periodic tasks
      Fixed rate (“isochronous”) flows (e.g. sensor data, speech)
      Characterize by inter-packet spacing, message length, reception deadline
    Can be generated by sporadic tasks
      Variable rate flows (e.g. MPEG-2 video, control traffic)
      Characterize by average throughput + maximum burst size
  Aperiodic (asynchronous) messages
    No deadline, best-effort delivery, but want to keep delays small
    Characterize by average delivery time

## Slide 5: Sources of Message Delays
Message delays on networks comprise the following components:
  Queuing delay at sender
    Network not always ready to accept a packet when it becomes available
    Data may be queued if produced faster than the network can deliver it
  Queuing delay in the network
    Due to cross-traffic or bottleneck links
  Network transit time
    Fixed propagation delay
  Queuing delay at receiver
    Application not always ready to accept packets arriving from network
    Network may deliver data in bursts

## Slide 6: Network Message Delay
Network
Network Interface
Transport Layer
Applications
1
2
4
Queueing delay at sender
Network transit time
Queueing delay at receiver
3
Network queueing delay

## Slide 7: Performance Metrics
Throughput: a measure of the number of packets that the network can deliver per unit time
Delay (latency): time taken to deliver a packet
  Fixed minimum propagation delay due to speed of light
  Variation due to queuing on path
Jitter: Variance of the delay
Buffer requirements: amount of storage required so as not to drop packets
Packet Miss rate: ratio of packets that miss their timing constraints
Packet Loss Rate: ratio of packets that are not delivered
Packet Error Rate: ratio of packets that have an error in them

## Slide 8: Throughput, Delay and Jitter
Network
Tx
Rx
Uniform inter-packet spacing
Non-uniform inter-packet spacing
(some packets delayed more than others)
Throughput, delay and jitter vary according to router scheduling techniques.
  Possible to derive bounds for delay/jitter for some policies (e.g. RMA, Round-Robin, Weighted Round-Robin techniques)

## Slide 9: Jitter and Miss-Rate
Want to characterize jitter distribution
  Hope for something approximating a Gaussian distribution ⇒ simple statistics to derive the miss rate
    Fraction of packets lost due to jitter
  Actual distribution is more complex
Packet Delay
Frequency of Occurrence
Ideal
Distribution
Gaussian Distribution
Actual Distribution
Minimum network delay
Discarded packets due to late arrival

## Slide 10: VW Passat Network Architecture
Often we find many different physical / MAC layers within a system…

## Slide 11: Congestion and Loss
Both flow characteristics and cross-traffic can cause overloads and congestion, so might the cross traffic
  Temporary congestion will cause queuing delays
  Persistent congestion will result in queues that stay full, hence packets may be lost
How to avoid this?
  Control the amount of traffic at a bottleneck link
    Applications need to signal their requirements
    Network performs admission control
  Or prioritize traffic to give preference to important flows
    What scheduling algorithm to use?
      Fixed-priority schemes are much easier to implement than dynamic priority schemes
      Weighted round-robin techniques are also available
    May allow real-time traffic, but discard best-effort data traffic when the network is overloaded

## Slide 12: Controller Area Networks (CANbus)
ID
Control
Data
Shared serial bus, send at 1Mbps, maximum bus length is 50m
All stations hear transmissions within a fraction of a bit time
Connections wired AND logic (zero will dominate) logic
Packets start with an ID, then control and data
Widely used in automotive
  Finding its way to other areas
Start of packet

## Slide 13: CAN bus: Wiring

## Slide 14: CAN Bus
Courtesy of TI sloa101 application note…
Bus Guardian

## Slide 15: CAN bus: Data Rate vs Distance

## Slide 16: Distributed Priority-based Arbitration
Wait until start of slot, then begin to send with the ID field, but:
Stop if you hear a 0 on the bus when you are sending a 1
Packet with the smallest ID is transmitted first
  Priority-based network access
Node 2 Loses
Node 1 Loses

## Slide 17: CAN bus: Packets

## Slide 18: Real-Time Analysis of CAN
Remember our CPU task model τi = { Ci, Ti }
In a communication system:
  Ci is the message transmission time
  Ti is the period of the message
What is different as compared to a CPU?
-------- + .... + --------- < U(n) = n(2 - 1)
C1+ B1 Cn+ Bn 1/ n
T1 Tn

## Slide 19: CAN bus Timing Analysis
Treat messages like priority-based tasks on a processor
  Perform RMA analysis
Messages have non-preemptible regions
  Adjust by adding blocking factors
Davis, et al “Controller Area Network (CAN) schedulability analysis: Refuted, revisited and revised” RTSJ, 2007

## Slide 20: Example: Ethernet
Recall that Ethernet uses CSMA/CD with exponential back off
  Before transmitting, check for active link
  If not active, try to transmit, listening for collision
  If a collision occurs, stop sending, wait before retry
  Random binary exponential back-off
    After i collisions, back-off by up to 2i slots, randomly chosen
Potentially unbounded delay on busy network
  Cannot schedule transmissions to avoid collision
No prioritization of messages
Implications:
  Throughput actually drops at high loads
  Cannot easily reason about timing properties
  Difficult to schedule messages to ensure timely delivery

## Slide 21: Real-Time Ethernet?
If you have control over ALL nodes in the system
Coordinate using Time Diversity Multiple Access (TDMA)
Synchronize each node (somehow) and assigned a time slot to transmit
Polling TDMA
Synchronized TDMA

## Slide 22: Priorities in non-Logical AND networks?
Use transmission delay to act like a priority
Low priority waits longer before it transmits
Node 1 (H)
Node 2 (M)
Node 3 (L)
Dynamic Start
Longer Delay -> Lower Priority

## Slide 23: Conclusions
What is real-time communications?
Factors that affect real-time communication
  Throughput, delay and jitter
  Clock skew
  Congestion and loss
Examples of networks and their timing properties
  Some networks (like CANbus) provide timing guarantees, others (like the ethernet) do not